## Slide 1: Lab Works

## Slide 2: Required Materials:
8085 Simulator or Kit
  https:;www.sim8085.com/
Programs

## Slide 3: Lab1: Understanding addressing modes in 8085 microprocessors.
Topics: Direct addressing, Indirect addressing
Write an ALP for 8085 MP to store an immediate 8-bit data in memory location 2051H using direct addressing.
Write an ALP for 8085 MP to store 8-bit data in memory 2501H using indirect addressing.

## Slide 4: Lab2: Addition with 8085 microprocessors.
Write an ALP for adding two 8-bit numbers 02H and 03H using immediate addressing . The result is to be stored in 1050 H.
Write an ALP for adding two 8-bit numbers stored in 2501H and 2502H. The result is to be stored in 2503H.
Write an assembly language program to add two 8-bit numbers (F1 and 15), stored at C050H and C051H, with carry.
Write an assembly language program to add two 16-bit numbers A645 and 9B23, stored from C050H onwards, with carry.

## Slide 5: Lab3: Subtraction with 8085 microprocessors.
Write an ALP for subtracting two 8-bit numbers stored in 2501H and 2502H. The result is to be stored in 2503H.

## Slide 6: Lab 4: Swapping of data with 8085 microprocessors.
Write a program in Assembly language to interchange(Swap) the contents of two memory location 2100H and 2101H.

## Slide 7: Lab 5: Multiplication with 8085 microprocessors.
Write a program in Assembly language to multiply two 8 bit numbers stored at C050H and C051H.

## Slide 8: Lab 6: Looping in 8085 programs
Write a program in Assembly language to find the square of a number stored at 8000H.
Write a program in Assembly language to print N natural numbers upto the number stored at 8000H. (ie. If 5, then the series should be 1,2,3,4,5)
Write a program in Assembly language to find the factorial of a number stored at 8000H and store the factorial at 8001H.

## Slide 9
5. Basic Assembly language programs of 8085

## Slide 10: 1. Write an ALP for 8085 MP to store an immediate 8-bit data in memory location 2051H using direct addressing.
MVI A,49H ; "Store 49H in the accumulator"
STA 2501H ;"Copy accumulator contents at address 2501H"
HLT ; "Stop"
Test Ok

## Slide 11: 2. Write an ALP for 8085 MP to store 8-bit data in memory 2501H using indirect addressing.
LXI H,2501H ; "Load H-L pair with 2501H"
MVI M,49H ; "Store 49H in memory location pointed by H-L register pair (2501H)"
HLT ; "Stop"
Test Ok

## Slide 12: 3. Write an ALP for adding two 8-bit numbers 02H and 03H using immediate addressing . The result is to be stored in 1050 H.
MVI A, 02H ; “Get the first number and move to accumulator”
MVI B, 03H ; “Get the second number and move to register B"
ADD B ; "Add the second number with the content of accumulator"
STA 1050H ; "Store result at 1050H"
HLT ; "Stop"
Test Ok

## Slide 13: 4. Write an ALP for adding two 8-bit numbers stored in 2501H and 2502H. The result is to be stored in 2503H.
LXI H, 2501H ; "Get address of first number in H-L pair. Now H-L points to 2501H"
MOV A, M ; "Get first operand in accumulator"
INX H ; "Increment content of H-L pair. Now, H-L points 2502H"
ADD M ; "Add first and second operand"
INX H ; "H-L points 2503H"
MOV M, A ; "Store result at 2503H"
HLT ; "Stop"
Test Ok

## Slide 14: 5. Write an ALP for subtracting two 8-bit numbers stored in 2501H and 2502H. The result is to be stored in 2503H.
LXI H, 2501H ; "Get address of first number in H-L pair. Now H-L points to 2501H"
MOV A, M ; "Get first operand in accumulator"
INX H ; "Increment content of H-L pair. Now, H-L points 2502H"
SUB M ; "Subtract first to second operand"
INX H ; "H-L points 2503H"
MOV M, A ; "Store result at 2503H"
HLT ; "Stop"
Test Ok

## Slide 15: 6. Write an assembly language program to add two 8-bit numbers (F1 and 15), stored at C050H and C051H, with carry.
LXI H, C050H ; "Get address of first number in H-L pair. Now H-L points to C050H"
MOV A, M ; "Get first operand in accumulator from C050H"
INX H ; "Increment content of H-L pair. Now, H-L points C051H"
MVI B, 00H ; “Initialize Register B with 00H for carry store”
ADD M ; "Add first and second operand, result stored in Acc"
JNC label ; “Jump to label if no carry”
INR B ; “Increment content of B by 1”
label: STA C053H ; “Store the content of Acc to C053H”
  MOV A, B ; “Move carry at Acc"
  STA C052H ; “Store the content of Acc to C052H, ie the carry part”
  HLT ; "Stop"
  ; “Carry part store in C052H and sum is store in C053H”
Reference: https:;www.youtube.com/watch?v=GLfEQGY70Ek&list=PLndX8heiWwErijxt7FpnRilO2KV4UhFmN
Test Ok

## Slide 16: 7. Write an assembly language program to add two 16-bit numbers A645 and 9B23, stored from C050H onwards, with carry.
LHLD C050H ; "Get address of first number from memory and load in in H-L register”
XCHG ; Exchange H and L with D and E
LHLD C052H ; "Get address of second number from memory and load in in H-L register”
MVI B, 00H ; “Initialize Register B with 00H for carry store”
DAD D ; Add both the register pairs and store in HL, ie. HL+DE
JNC label ; “Jump to label if no carry”
INR B ; “Increment content of B by 1”
label: SHLD C054H ; “Store the content of H-L register to C054H”
  MOV A, B ; “Move carry at Acc"
  STA C056H ; “Store the content of Acc to C056H, ie the carry part”
  HLT ; "Stop"
  ; “Carry part store in C056H and sum is store in C054H-C055H”
Reference: https:;www.youtube.com/watch?v=_4Q-upoIv8c&list=PLndX8heiWwErijxt7FpnRilO2KV4UhFmN&index=2
Test Ok

## Slide 17: 8. Write a program in Assembly language to interchange(Swap) the contents of two memory location 2100H and 2101H.
LDA 2100H ; “Load the content of 2100H into Accumulator”
MOV B,A ; “Move content of Acc to register B”
LDA 2101H ;“Load content of 2101H to Accumulator”
STA 2100H ; “Store content of Acc. to 2100H”
MOV A,B ; “Move content of register B to Acc.”
STA 2101H ; “Store content of Acc. To 2101H”
HLT ; “End”
Test Ok

## Slide 18: 8. Write a program in Assembly language to multiply two 8 bit numbers stored at C050H and C051H.
LXI H,C050H ; Get address of first number in H-L pair. Now H-L points to C050H"
MOV B,M ; Get first operand in register B from C050H"
MVI A,00H ;Clear Accumulator
MVI D, 00H ;Initialize a register D with 00H for carry storage
INX H ; point to C051H
MOV C,M ;Get the second operand
loop1: ADD B ;Add contents in register B with Accumulator
JNC loop2 ; Jump to loop2 if no carry
INR D ;increase D
loop2: DCR C ;Decrement counter C
JNZ loop1 ;Jump to loop1 if C not equal to 0
STA C052H ;Store the content to C052H
MOV A,D ;Move D to A.
STA C053H ;Store content of Acc. To C053.
HLT
Test Ok
5x3*15
5+5+5=15

## Slide 19: 9. Write a program in Assembly language to find the square of a number stored at 8000H.
LXI H,8000H ;Load the number from 8000H
XRA A ;Clear accumulator
MOV B,M ;Load data from memory to B
LOOP: ADD M ;Add memory byte with A
DCR B ;Decrease B by 1
JNZ LOOP ;jump to loop if B not equal to 0
STA 8050H ;Store result into memory
HLT ; Terminate the program
Note: This finding of square of a number n is done by adding the numbers for n times in the accumulator.
Test Ok

## Slide 20: 10. Write a program in Assembly language to print N natural numbers upto the number stored at 8000H. (ie. If 5, then the series should be 1,2,3,4,5)
LXI H, 8000H ;Load the number store at 8000H
MOV B,M ;Take number from memory to B
MVI D, 01H ;Set D to 01H
loop: ADD D ;Add content in D to Accumulator
INX H ;Increase the pointer to next memory location
MOV M,A ;Move content of Accumulator to memory
DCR B ;Decrease B by 1
JNZ loop ;Jump to loop if B not equal to 0
HLT ;Terminate the program
Test Ok

## Slide 21: 11. Write a program in Assembly language to find the factorial of a number stored at 8000H and store the factorial at 8001H.
;Main program
LXI H, 8000H ;Load the number store at 8000H
MOV B,M ;Take number from memory to B
MVI D, 01H ;Set D to 01H
FACT: CALL MUL ;Call multiplication subroutine
DCR B ;Decrease B by 1
JNZ FACT ;If Z = 0, jump to Fact
INX H ;Point to next location
MOV M,D ;Store result in memory
HLT ;Terminate the program
;Sub Program1
MUL: MOV E,B ;Load B to E
XRA A ;Clear accumulator to store result
;Sub Program2
ML: ADD D ;Add D to A
DCR E ;Decrement E
JNZ ML ;If Z = 0, jump to ML
MOV D,A ;Transfer contents of A to D
RET ;Return result
Note: This finding of factorial of a number n is done by successive addition using nested looping.
Test Ok

## Slide 22
The End