## Slide 2: MICROPROCESSOR 8085
Reference Book:
– Ramesh S. Goankar, “Microprocessor Architecture, Programming and Applications with 8085”, 5th Edition, Prentice Hall
Week 1 – Basic Concept and Ideas about Microprocessor.
Week 2 - Architecture of 8085
Week 3 - Addressing Modes and Instruction set of 8085
Week 4 – Interrupts of 8085
Week 5 onwards – Peripherals.

## Slide 3: Basic Concepts of Microprocessors
Differences between:
  Microcomputer – a computer with a microprocessor as its CPU. Includes memory, I/O etc.
  Microprocessor – silicon chip which includes ALU, register circuits & control circuits
  Microcontroller – silicon chip which includes microprocessor, memory & I/O in a single package.

## Slide 4: What is a Microprocessor?
The word comes from the combination micro and processor.
  Processor means a device that processes whatever. In this context processor means a device that processes numbers, specifically binary numbers, 0’s and 1’s.
    To process means to manipulate. It is a general term that describes all manipulation. Again in this content, it means to perform certain operations on the numbers that depend on the microprocessor’s design.

## Slide 5: What about micro?
Micro is a new addition.
  In the late 1960’s, processors were built using discrete elements.
    These devices performed the required operation, but were too large and too slow.
  In the early 1970’s the microchip was invented. All of the components that made up the processor were now placed on a single piece of silicon. The size became several thousand times smaller and the speed became several hundred times faster. The “Micro”Processor was born.

## Slide 6: Was there ever a “mini”- processor?
No.
– It went directly from discrete elements to a single chip. However, comparing today’s microprocessors to the ones built in the early 1970’s you find an extreme increase in the amount of integration.
So, What is a microprocessor?

## Slide 7: Definition of the Microprocessor
The microprocessor is a programmable device that takes in numbers, performs on them arithmetic or logical operations according to the program stored in memory and then produces other numbers as a result.

## Slide 8: Definition (Contd.)
Lets expand each of the underlined words:
  Programmable device: The microprocessor can perform different sets of operations on the data it receives depending on the sequence of instructions supplied in the given program.
By changing the program, the microprocessor manipulates
the data in different ways.
  Instructions: Each microprocessor is designed to execute a specific group of operations. This group of operations is called an instruction set. This instruction set defines what the microprocessor can and cannot do.

## Slide 9: Definition (Contd.)
Takes in: The data that the microprocessor manipulates must come from somewhere.
  It comes from what is called “input devices”.
  These are devices that bring data into the system from the outside world.
  These represent devices such as a keyboard, a mouse, switches, and the like.

## Slide 10: Definition (Contd.)
– Numbers: The microprocessor has a very narrow view on life. It only understands binary numbers.
A binary digit is called a bit (which comes from binary digit).
The microprocessor recognizes and processes a group of bits together. This group of bits is called a “word”.
The number of bits in a Microprocessor’s word, is a measure of its “abilities”.

## Slide 11: Definition (Contd.)
Words, Bytes, etc.
  The earliest microprocessor (the Intel 8088 and Motorola’s 6800) recognized 8-bit words.
    They processed information 8-bits at a time. That’s why they are called “8-bit processors”. They can handle large numbers, but in order to process these numbers, they broke them into 8-bit pieces and processed each group of 8-bits separately.
  Later microprocessors (8086 and 68000) were designed with 16-bit words.
    A group of 8-bits were referred to as a “half-word” or “byte”.
    A group of 4 bits is called a “nibble”.
    Also, 32 bit groups were given the name “long word”.
  Today, all processors manipulate at least 32 bits at a time and there exists microprocessors that can process 64, 80, 128 bits

## Slide 12: Definition (Contd.)
Arithmetic and Logic Operations:
  Every microprocessor has arithmetic operations such as add and subtract as part of its instruction set.
    Most microprocessors will have operations such as multiply and divide.
    Some of the newer ones will have complex operations such as square root.
  In addition, microprocessors have logic operations as well. Such as AND, OR, XOR, shift left, shift right, etc.
  Again, the number and types of operations define the microprocessor’s instruction set and depends on the specific microprocessor.

## Slide 13: Definition (Contd.)
Stored in memory :
  First, what is memory?
    Memory is the location where information is kept while not in current use.
    Memory is a collection of storage devices. Usually, each storage device holds one bit. Also, in most kinds of memory, these storage devices are grouped into groups of 8. These 8 storage locations can only be accessed together. So, one can only read or write in terms of bytes to and form memory.
    Memory is usually measured by the number of bytes it can hold.
It is measured in Kilos, Megas and lately Gigas. A Kilo in computer language is 210 =1024. So, a KB (KiloByte) is 1024 bytes. Mega is 1024 Kilos and Giga is 1024 Mega.

## Slide 14: Definition (Contd.)
Stored in memory:
  When a program is entered into a computer, it is stored in memory. Then as the microprocessor starts to execute the instructions, it brings the instructions from memory one at a time.
  Memory is also used to hold the data.
– The microprocessor reads (brings in) the data from memory when it needs it and writes (stores) the results into memory when it is done.

## Slide 15: Definition (Contd.)
Produces: For the user to see the result of the execution of the program, the results must be presented in a human readable form.
  The results must be presented on an output device.
  This can be the monitor, a paper from the printer, a simple LED or many other forms.

## Slide 16: A Microprocessor-based system
Memory
Output
Input
From the above description, we can draw the following block diagram to represent a microprocessor-based system:

## Slide 17: Inside The Microprocessor
Internally, the microprocessor is made up of 3 main units.
  The Arithmetic/Logic Unit (ALU)
  The Control Unit.
  An array of registers for holding data while it is being manipulated.

## Slide 18: Organization of a microprocessor- based system
I/O Input / Output
Memory
ROM RAM
System Bus
ALU | Register Array
Control | 
Let’s expand the picture a bit.

## Slide 19: Memory
Memory stores information such as instructions and data in binary format (0 and 1). It provides this information to the microprocessor whenever it is needed.
Usually, there is a memory “sub-system” in a microprocessor-based system. This sub-system includes:
  The registers inside the microprocessor
  Read Only Memory (ROM)
    used to store information that does not change.
  Random Access Memory (RAM) (also known as Read/Write Memory).
    used to store information supplied by the user. Such as programs and data.

## Slide 20: Memory Map and Addresses
FFFF
Address Range
EPROM
RAM 1
RAM 2
RAM 3
RAM 4
The memory map is a picture representation of the address range and shows where the different memory chips are located within the address range.
0000 0000
8FFF
9000
A3FF A400
Address Range of EPROM Chip
3FFF
4400
Address Range of 1st RAM Chip
5FFF
6000
Address Range of 2nd RAM Chip
Address Range of 3rd RAM Chip
Address Range of 4th RAM Chip
F7FF

## Slide 21: Memory
To execute a program:
  the user enters its instructions in binary format into the memory.
  The microprocessor then reads these instructions and whatever data is needed from memory, executes the instructions and places the results either in memory or produces it on an output device.

## Slide 22: The three cycle instruction execution model
To execute a program, the microprocessor “reads” each instruction from memory, “interprets” it, then “executes” it.
To use the right names for the cycles:
  The microprocessor fetches each instruction,
  decodes it,
  Then executes it.
This sequence is continued until all instructions are performed.

## Slide 23: Machine Language
The number of bits that form the “word” of a microprocessor is fixed for that particular processor.
  These bits define a maximum number of combinations.
    For example an 8-bit microprocessor can have at most 28 = 256 different combinations.
However, in most microprocessors, not all of these combinations are used.
  Certain patterns are chosen and assigned specific meanings.
  Each of these patterns forms an instruction for the microprocessor.
  The complete set of patterns makes up the microprocessor’s machine language.

## Slide 24: The 8085 Machine Language
The 8085 (from Intel) is an 8-bit microprocessor.
  The 8085 uses a total of 246 bit patterns to form its instruction set.
  These 246 patterns represent only 74 instructions.
    The reason for the difference is that some (actually most) instructions have multiple different formats.
  Because it is very difficult to enter the bit patterns correctly, they are usually entered in hexadecimal instead of binary.
    For example, the combination 0011 1100 which translates into “increment the number in the register called the accumulator”, is usually entered as 3C.

## Slide 25: Assembly Language
Entering the instructions using hexadecimal is quite easier than entering the binary combinations.
  However, it still is difficult to understand what a program written in hexadecimal does.
  So, each company defines a symbolic code for the instructions.
  These codes are called “mnemonics”.
  The mnemonic for each instruction is usually a group of letters that suggest the operation performed.

## Slide 26: Assembly Language
Using the same example from before,
  00111100 translates to 3C in hexadecimal (OPCODE)
  Its mnemonic is: “INR A”.
  INR stands for “increment register” and A is short for accumulator.
Another example is: 1000 0000,
  Which translates to 80 in hexadecimal.
  Its mnemonic is “ADD B”.
  “Add register B to the accumulator and keep the result in the accumulator”.

## Slide 27: Assembly Language
It is important to remember that a machine language and its associated assembly language are completely machine dependent.
  In other words, they are not transferable from one microprocessor to a different one.
For example, Motorolla has an 8-bit microprocessor called the 6800.
  The 8085 machine language is very different from that of the 6800. So is the assembly language.
  A program written for the 8085 cannot be executed on the 6800 and vice versa.

## Slide 28: “Assembling” The Program
How does assembly language get translated into machine language?
  There are two ways:
  1st there is “hand assembly”.
    The programmer translates each assembly language instruction into its equivalent hexadecimal code (machine language). Then the hexadecimal code is entered into memory.
  The other possibility is a program called an “assembler”, which does the translation automatically.

## Slide 29: 8085 Microprocessor Architecture
8-bit general purpose µp
Capable of addressing 64 k of memory
Has 40 pins
Requires +5 v power supply
Can operate with 3 MHz clock
8085 upward compatible

## Slide 30: Pins
Frequency Generator is connected to those pins
Power Supply: +5 V
Address latch Enable
Read
Write
Input/Output/ Memory
Multiplexed Address Data Bus
Address Bus

## Slide 32
System Bus – wires connecting memory & I/O to microprocessor
  Address Bus
    Unidirectional
    Identifying peripheral or memory location
  Data Bus
    Bidirectional
    Transferring data
  Control Bus
    Synchronization signals
    Timing signals
    Control signal

## Slide 33: Architecture of Intel 8085 Microprocessor

## Slide 34: Intel 8085 Microprocessor
Microprocessor consists of:
  Control unit: control microprocessor operations.
  ALU: performs data processing function.
  Registers: provide storage internal to CPU.
  Interrupts
  Internal data bus

## Slide 35: The ALU
In addition to the arithmetic & logic circuits, the ALU includes the accumulator, which is part of every arithmetic & logic operation.
Also, the ALU includes a temporary register used for holding data temporarily during the execution of the operation. This temporary register is not accessible by the programmer.

## Slide 36
Registers
  General Purpose Registers
    B, C, D, E, H & L (8 bit registers)
    Can be used singly
    Or can be used as 16 bit register pairs
      BC, DE, HL
    H & L can be used as a data pointer (holds memory address)
  Special Purpose Registers
    Accumulator (8 bit register)
      Store 8 bit data
      Store the result of an operation
Accumulator | Flags
B | C
D | E
H | L
Program Counter | 
Stack Pointer | 
– Store 8 bit data during I/O transfer Address
8 Data
16

## Slide 37
Flag Register
  8 bit register – shows the status of the microprocessor before/after an operation
  S (sign flag), Z (zero flag), AC (auxillary carry flag), P (parity flag) & CY (carry flag)
Sign Flag
  Used for indicating the sign of the data in the accumulator
  The sign flag is set if negative (1 – negative)
  The sign flag is reset if positive (0 –positive)
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
S | Z | X | AC | X | P | X | CY

## Slide 38
Carry Flag
– Is set if there is a carry or borrow from arithmetic operation
Zero Flag
  Is set if result obtained after an operation is 0
  Is set following an increment or decrement operation of that register
10110011
+ 01001101
1 00000000
Carry 1
0010 0001
1011 0101 |  | 1011 0101
+ 0110 1100 | - | 1100 1100
Borrow 1
1110 1001

## Slide 39
Auxillary Carry Flag
  Is set if there is a carry out of bit 3
Parity Flag
  Is set if parity is even
  Is cleared if parity is odd

## Slide 40: The Internal Architecture
We have already discussed the general purpose registers, the Accumulator, and the flags.
The Program Counter (PC)
  This is a register that is used to control the sequencing of the execution of instructions.
  This register always holds the address of the next instruction.
  Since it holds an address, it must be 16 bits wide.

## Slide 41: The Internal Architecture
The Stack pointer
  The stack pointer is also a 16-bit register that is used to point into memory.
  The memory this register points to is a special area called the stack.
  The stack is an area of memory used to hold data that will be retreived soon.
  The stack is usually accessed in a Last In First Out (LIFO) fashion.

## Slide 42: Non Programmable Registers
Instruction Register & Decoder
  Instruction is stored in IR after fetched by processor
  Decoder decodes instruction in IR
Internal Clock generator
  3.125 MHz internally
  6.25 MHz externally

## Slide 43: The Address and Data Busses
The address bus has 8 signal lines A8 – A15 which are unidirectional.
The other 8 address bits are multiplexed (time shared) with the 8 data bits.
  So, the bits AD0 – AD7 are bi-directional and serve as A0 – A7 and D0 – D7 at the same time.
    During the execution of the instruction, these lines carry the address bits during the early part, then during the late parts of the execution, they carry the 8 data bits.
  In order to separate the address from the data, we can use a latch to save the value before the function of the bits changes.

## Slide 44: Demultiplexing AD7-AD0
From the above description, it becomes obvious that the AD7– AD0 lines are serving a dual purpose and that they need to be demultiplexed to get all the information.
The high order bits of the address remain on the bus for three clock periods. However, the low order bits remain for only one clock period and they would be lost if they are not saved externally. Also, notice that the low order bits of the address disappear when they are needed most.
To make sure we have the entire address for the full three clock cycles, we will use an external latch to save the value of AD7– AD0 when it is carrying the address bits. We use the ALE signal to enable this latch.

## Slide 45: Demultiplexing AD7-AD0
– Given that ALE operates as a pulse during T1, we will be able to latch the address. Then when ALE goes low, the address is saved and the AD7– AD0 lines can be used for their purpose as the bi-directional data lines.
A15-A8
Latch
AD7-AD0
D7- D0
A7- A0
8085
ALE

## Slide 46: Demultiplexing the Bus AD7 – AD0
The high order address is placed on the address bus and hold for 3 clk periods,
The low order address is lost after the first clk period, this address needs to be hold however we need to use latch
The address AD7 – AD0 is connected as inputs to the latch 74LS373.
The ALE signal is connected to the enable (G) pin of the latch and the OC – Output control – of the latch is grounded

## Slide 48: The Overall Picture
Putting all of the concepts together, we get:
A15-A8
Latch
AD7-AD0
D7- D0
A7- A0
8085
ALE
WR RD IO/M
CS
1K Byte Memory Chip
RD WR
A9- A0
A15- A10
Chip Selection Circuit

## Slide 49: Introduction to 8085 Instructions

## Slide 50: The 8085 Instructions
Since the 8085 is an 8-bit device it can have up to 28
(256) instructions.
  However, the 8085 only uses 246 combinations that represent a total of 74 instructions.
– Most of the instructions have more than one format.
These instructions can be grouped into five different groups:
  Data Transfer Operations
  Arithmetic Operations
  Logic Operations
  Branch Operations
  Machine Control Operations

## Slide 51: Instruction and Data Formats
Each instruction has two parts.
  The first part is the task or operation to be performed.
    This part is called the “opcode” (operation code).
  The second part is the data to be operated on
    Called the “operand”.

## Slide 52: Data Transfer Operations
These operations simply COPY the data from the source to the destination.
MOV, MVI, LDA, and STA
They transfer:
  Data between registers.
  Data Byte to a register or memory location.
  Data between a memory location and a register.
  Data between an I\O Device and the accumulator.
– The data in the source is not changed.

## Slide 53: The LXI instruction
The 8085 provides an instruction to place the 16-bit data into the register pair in one step.
  LXI Rp, <16-bit address> (Load eXtended Immediate)
The instruction LXI B 4000H will place the 16-bit number 4000 into the register pair B, C.
  The upper two digits are placed in the 1st register of the pair and the lower two digits in the 2nd .
40
00
LXI B 40 00H
B
C

## Slide 54: The Memory “Register”
Most of the instructions of the 8085 can use a memory location in place of a register.
  The memory location will become the “memory” register M.
    MOV M B
– copy the data from register B into a memory location.
  Which memory location?
The memory location is identified by the contents of the HL register pair.
  The 16-bit contents of the HL register pair are treated as a 16-bit address and used to identify the memory location.

## Slide 55: Using the Other Register Pairs
There is also an instruction for moving data from memory to the accumulator without disturbing the contents of the H and L register.
  LDAX Rp (LoaD Accumulator eXtended)
    Copy the 8-bit contents of the memory location identified by the Rp register pair into the Accumulator.
    This instruction only uses the BC or DE pair.
    It does not accept the HL pair.

## Slide 56: Indirect Addressing Mode
Using data in memory directly (without loading first into a Microprocessor’s register) is called Indirect Addressing.
Indirect addressing uses the data in a register pair as a 16-bit address to identify the memory location being accessed.
  The HL register pair is always used in conjunction with the memory register “M”.
  The BC and DE register pairs can be used to load data into the Accumultor using indirect addressing.

## Slide 57: Arithmetic Operations
Addition (ADD, ADI):
  Any 8-bit number.
  The contents of a register.
  The contents of a memory location.
Can be added to the contents of the accumulator and the result is stored in the accumulator.
Subtraction (SUB, SUI):
  Any 8-bit number
  The contents of a register
  The contents of a memory location
Can be subtracted from the contents of the accumulator. The result is stored in the accumulator.

## Slide 58: Arithmetic Operations Related to Memory
These instructions perform an arithmetic operation using the contents of a memory location while they are still in memory.
  ADD M
    Add the contents of M to the Accumulator
  SUB M
    Sub the contents of M from the Accumulator
  INR M / DCR M
    Increment/decrement the contents of the memory location in place.
  All of these use the contents of the HL register pair to identify the memory location being used.

## Slide 59: Arithmetic Operations
Increment (INR) and Decrement (DCR):
  The 8-bit contents of any memory location or any register can be directly incremented or decremented by 1.
  No need to disturb the contents of the accumulator.

## Slide 60: Manipulating Addresses
Now that we have a 16-bit address in a register pair, how do we manipulate it?
– It is possible to manipulate a 16-bit address stored in a register pair as one entity using some special instructions.
INX Rp
DCX Rp
(Increment the 16-bit number in the register pair) (Decrement the 16-bit number in the register pair)
– The register pair is incremented or decremented as one entity. No need to worry about a carry from the lower 8-bits to the upper. It is taken care of automatically.

## Slide 61: Logic Operations
These instructions perform logic operations on the contents of the accumulator.
  ANA, ANI, ORA, ORI, XRA and XRI
    Source: Accumulator and
      An 8-bit number
      The contents of a register
      The contents of a memory location
    Destination: Accumulator
ANA | R/M | AND Accumulator With Reg/Mem
ANI | # | AND Accumulator With an 8-bit number
ORA | R/M | OR Accumulator With Reg/Mem
ORI | # | OR Accumulator With an 8-bit number
XRA | R/M | XOR Accumulator With Reg/Mem
XRI | # | XOR Accumulator With an 8-bit number

## Slide 62: Logic Operations
Complement:
  1’s complement of the contents of the accumulator.
CMA No operand

## Slide 63: Additional Logic Operations
Rotate
– Rotate the contents of the accumulator one position to the left or right.
RLC
RAL
RRC
RAR
Rotate the accumulator left.
Bit 7 goes to bit 0 AND the Carry flag.
Rotate the accumulator left through the carry. Bit 7 goes to the carry and carry goes to bit 0.
Rotate the accumulator right.
Bit 0 goes to bit 7 AND the Carry flag.
Rotate the accumulator right through the carry. Bit 0 goes to the carry and carry goes to bit 7.

## Slide 64: RLC vs. RLA
RLC
RAL
Accumulator
Carry Flag
7
6
5
4
3
2
1
0
Accumulator
Carry Flag
7
6
5
4
3
2
1
0

## Slide 65: Logical Operations
Compare
  Compare the contents of a register or memory location with the contents of the accumulator.
– CMP | R/M | Compare the contents of the register or memory location to the contents of the accumulator.
– CPI | # | Compare the 8-bit number to the contents of the accumulator.
The compare instruction sets the flags (Z, Cy, and S).
The compare is done using an internal subtraction that does not change the contents of the accumulator.
A – (R / M / #)

## Slide 66: Branch Operations
Two types:
  Unconditional branch.
    Go to a new location no matter what.
  Conditional branch.
    Go to a new location if the condition is true.

## Slide 67: Unconditional Branch
– JMP
Address
Jump to the address specified (Go to).
CALL Address
  Jump to the address specified but treat it as a subroutine.
RET
  Return from a subroutine.
– The addresses supplied to all branch operations must be 16-bits.

## Slide 68: Conditional Branch
Go to new location if a specified condition is met.
  JZ Address (Jump on Zero)
    Go to address specified if the Zero flag is set.
  JNZ Address (Jump on NOT Zero)
    Go to address specified if the Zero flag is not set.
  JC Address (Jump on Carry)
    Go to the address specified if the Carry flag is set.
  JNC Address (Jump on No Carry)
    Go to the address specified if the Carry flag is not set.
  JP Address (Jump on Plus)
    Go to the address specified if the Sign flag is not set
  JM Address (Jump on Minus)
    Go to the address specified if the Sign flag is set.

## Slide 69: Machine Control
HLT
  Stop executing the program.
NOP
  No operation
  Exactly as it says, do nothing.
  Usually used for delay or to replace instructions during debugging.

## Slide 70: Operand Types
There are different ways for specifying the operand:
  There may not be an operand (implied operand)
    CMA
  The operand may be an 8-bit number (immediate data)
    ADI 4FH
  The operand may be an internal register (register)
    SUB B
  The operand may be a 16-bit address (memory address)
    LDA 4000H

## Slide 71: Instruction Size
Depending on the operand type, the instruction may have different sizes. It will occupy a different number of memory bytes.
  Typically, all instructions occupy one byte only.
  The exception is any instruction that contains immediate data or a memory address.
    Instructions that include immediate data use two bytes.
      One for the opcode and the other for the 8-bit data.
    Instructions that include a memory address occupy three bytes.
      One for the opcode, and the other two for the 16-bit address.

## Slide 72: Instruction with Immediate Date
Operation: Load an 8-bit number into the accumulator.
  MVI A, 32
    Operation: MVI A
    Operand: The number 32
    Binary Code:
2nd
0011 1110 3E 1st byte.
0011 0010 32 byte.

## Slide 73: Instruction with a Memory Address
Operation: go to address 2085.
  Instruction: JMP 2085
    Opcode: JMP
    Operand: 2085
    Binary code:
1100 0011 C3 1st byte.
1000 0101 | 85 | 2nd byte
0010 0000 | 20 | 3rd byte

## Slide 74: Addressing Modes
The microprocessor has different ways of specifying the data for the instruction. These are called “addressing modes”.
The 8085 has four addressing modes:
Implied
Immediate
Direct
Indirect
CMA MVI B, 45
LDA 4000 LDAX B
Load the accumulator with the contents of the memory location whose address is stored in the register pair BC).

## Slide 75: Data Formats
In an 8-bit microprocessor, data can be represented in one of four formats:
  ASCII
  BCD
  Signed Integer
  Unsigned Integer.
It is important to recognize that the microprocessor deals with 0’s and 1’s.
  It deals with values as strings of bits.
  It is the job of the user to add a meaning to these strings.

## Slide 76: Data Formats
Assume the accumulator contains the following value: 0100 0001.
  There are four ways of reading this value:
    It is an unsigned integer expressed in binary, the equivalent decimal number would be 65.
    It is a number expressed in BCD (Binary Coded Decimal) format. That would make it, 41.
    It is an ASCII representation of a letter. That would make it the letter A.
    It is a string of 0’s and 1’s where the 0th and the 6th bits are set to 1 while all other bits are set to 0.
ASCII stands for American Standard Code for Information Interchange.

## Slide 78: Counters & Time Delays

## Slide 79: Counters
A loop counter is set up by loading a register with a certain value
Then using the DCR (to decrement) and INR (to increment) the contents of the register are updated.
A loop is set up with a conditional jump instruction that loops back or not depending on whether the count has reached the termination count.

## Slide 80: Counters
The operation of a loop counter can be described using the following flowchart.
Initialize
Update the count
Is this Final Count?
Body of loop
No
Yes

## Slide 81: Sample ALP for implementing a loop Using DCR instruction
MVI C, 15H
LOOP
DCR C JNZ LOOP

## Slide 82: Using a Register Pair as a Loop Counter
Using a single register, one can repeat a loop for a maximum count of 255 times.
It is possible to increase this count by using a register pair for the loop counter instead of the single register.
  A minor problem arises in how to test for the final count since DCX and INX do not modify the flags.
  However, if the loop is looking for when the count becomes zero, we can use a small trick by ORing the two registers in the pair and then checking the zero flag.

## Slide 83: Using a Register Pair as a Loop Counter
The following is an example of a loop set up with a register pair as the loop counter.
LXI B, 1000H LOOP DCX B
MOV A, C ORA B JNZ LOOP

## Slide 84: Delays
It was shown in Chapter 2 that each instruction passes through different combinations of Fetch, Memory Read, and Memory Write cycles.
Knowing the combinations of cycles, one can calculate how long such an instruction would require to complete.
The table in Appendix F of the book contains a column with the title B/M/T.
  B for Number of Bytes
  M for Number of Machine Cycles
  T for Number of T-State.

## Slide 85: Delays
Knowing how many T-States an instruction requires, and keeping in mind that a T-State is one clock cycle long, we can calculate the time using the following formula:
Delay = No. of T-States / Frequency
For example a “MVI” instruction uses 7 T-States. Therefore, if the Microprocessor is running at 2 MHz, the instruction would require 3.5 Seconds to complete.

## Slide 86: Delay loops
We can use a loop to produce a certain amount of time delay in a program.
The following is an example of a delay loop:
MVI C, FFH LOOP DCR C
JNZ LOOP
7 T-States
4 T-States
10 T-States
The first instruction initializes the loop counter and is executed only once requiring only 7 T-States.
The following two instructions form a loop that requires 14 T-States to execute and is repeated 255 times until C becomes 0.

## Slide 87: Delay Loops (Contd.)
We need to keep in mind though that in the last iteration of the loop, the JNZ instruction will fail and require only 7 T-States rather than the 10.
Therefore, we must deduct 3 T-States from the total delay to get an accurate delay calculation.
To calculate the delay, we use the following formula:
Tdelay = TO + TL
  Tdelay = total delay
  TO = delay outside the loop
  TL = delay of the loop
TO is the sum of all delays outside the loop.

## Slide 88: Delay Loops (Contd.)
Using these formulas, we can calculate the time delay for the previous example:
TO = 7 T-States
  Delay of the MVI instruction
TL = (14 X 255) - 3 = 3567 T-States
  14 T-States for the 2 instructions repeated 255 times (FF16 = 25510) reduced by the 3 T-States for the final JNZ.

## Slide 89: Using a Register Pair as a Loop Counter
Using a single register, one can repeat a loop for a maximum count of 255 times.
It is possible to increase this count by using a register pair for the loop counter instead of the single register.
  A minor problem arises in how to test for the final count since DCX and INX do not modify the flags.
  However, if the loop is looking for when the count becomes zero, we can use a small trick by ORing the two registers in the pair and then checking the zero flag.

## Slide 90: Using a Register Pair as a Loop Counter
The following is an example of a delay loop set up with a register pair as the loop counter.
LXI B, 1000H LOOP DCX B
MOV A, C ORA B JNZ LOOP
10 T-States
6 T-States
4 T-States
4 T-States
10 T-States

## Slide 91: Using a Register Pair as a Loop Counter
Using the same formula from before, we can calculate:
TO = 10 T-States
  The delay for the LXI instruction
TL = (24 X 4096) - 3 = 98301 T- States
  24 T-States for the 4 instructions in the loop repeated 4096 times (100016 = 409610) reduced by the 3 T- States for the JNZ in the last iteration.

## Slide 92: Nested Loops
Nested loops can be easily setup in Assembly language by using two registers for the two loop counters and updating the right register in the right loop.
– In the figure, the body of loop2 can be before or after loop1.
Initialize loop 1
Update the count1
Is this Final Count?
Body of loop 1
No
Yes
Initialize loop 2
Body of loop 2
Update the count 2
Is this Final Count?
No
Yes

## Slide 93: Nested Loops for Delay
Instead (or in conjunction with) Register Pairs, a nested loop structure can be used to increase the total delay produced.
 | MVI B, 10H | 7 T-States
LOOP2 | MVI C, FFH | 7 T-States
LOOP1 | DCR C | 4 T-States
 | JNZ LOOP1 | 10 T-States
 | DCR B | 4 T-States
 | JNZ LOOP2 | 10 T-States

## Slide 94: Delay Calculation of Nested Loops
The calculation remains the same except that it the formula must be applied recursively to each loop.
  Start with the inner loop, then plug that delay in the calculation of the outer loop.
Delay of inner loop
  TO1 = 7 T-States
    MVI C, FFH instruction
– TL1 = (255 X 14) - 3 = 3567 T-States
    14 T-States for the DCR C and JNZ instructions repeated 255 times (FF = 255 ) minus 3 for the final JNZ

## Slide 95: Delay Calculation of Nested Loops
Delay of outer loop
  TO2 = 7 T-States
    MVI B, 10H instruction
– TL1 = (16 X (14 + 3574)) - 3 = 57405 T-States
    14 T-States for the DCR B and JNZ instructions and 3574
T-States for loop1 repeated 16 times (1016 = 1610) minus 3 for the final JNZ.
– TDelay = 7 + 57405 = 57412 T-States
Total Delay
– TDelay = 57412 X 0.5 Sec = 28.706 mSec

## Slide 96: Increasing the delay
The delay can be further increased by using register pairs for each of the loop counters in the nested loops setup.
It can also be increased by adding dummy instructions (like NOP) in the body of the loop.

## Slide 98: Timing Diagram
Representation of Various Control signals generated during Execution of an Instruction.
Following Buses and Control Signals must be shown in a Timing Diagram:
Higher Order Address Bus.
Lower Address/Data bus
ALE
RD
WR
IO/M

## Slide 99: Timing Diagram
Instruction: A000h
MOV A,B
Corresponding Coding: A000h 78

## Slide 100: Timing Diagram
Instruction:
A000h MOV A,B
Corresponding Coding: A000h 78
8085
Memory
OFC

## Slide 101: Timing Diagram
ALE
RD
WR
IO/M
T1
T2
T3
T4
A0h
A15- A8 (Higher Order Address bus)
00h 78h
Instruction:
A000h MOV A,B
Corresponding Coding: A000h 78
8085
Memory
OFC
Op-code fetch Cycle

## Slide 102: Timing Diagram
Instruction:
A000h MVI A,45h
Corresponding Coding:
A000h A001h
3E
45

## Slide 103: Timing Diagram
Instruction:
A000h MVI A,45h
Corresponding Coding:
A000h A001h
3E
45
OFC | 
MEMR | 
8085
Memory

## Slide 104: Timing Diagram
01h
45h
A0h
A15- A8 (Higher Order Address bus)
00h 3Eh
DA7-DA0 (Lower order address/data Bus)
ALE
RD
WR
IO/M
Op-Code Fetch Cycle
Memory Read Cycle
T1
T2
T3
T4
T5
T6
T7
A0h
Instruction:
A000h MVI A,45h
Corresponding Coding:
A000h A001h
3E
45

## Slide 105: Timing Diagram
Instruction:
A000h LXI A,FO45h
Corresponding Coding:
A000h A001h A002h
21
45
F0

## Slide 106: Timing Diagram
Instruction:
A000h LXI A,FO45h
Corresponding Coding:
A000h A001h A002h
21
45
F0
OFC | 
MEMR | 
MEMR | 
8085
Memory

## Slide 107: Memory Read Cycle
Timing Diagram
T1
T2
T3
T4
T5
T6
T7
T8
T9
T10
21h
01h
45h
02h
F0h
A0h
A0h
A0h
A15- A8 (Higher Order Address bus)
DA7-DA0 (Lower order address/data Bus)
ALE
RD
WR
IO/M
00h
Op-Code Fetch Cycle
Memory Read Cycle

## Slide 108: Timing Diagram
Instruction:
A000h MOV A,M
Corresponding Coding: A000h 7E

## Slide 109: Timing Diagram
OFC | 
MEMR | 
8085
Memory
Instruction:
A000h MOV A,M
Corresponding Coding: A000h 7E

## Slide 110: Timing Diagram
L Reg
Content Of M
A15- A8 (Higher Order Address bus)
00h 7Eh
DA7-DA0 (Lower order address/data Bus)
ALE
RD
WR
IO/M
Op-Code Fetch Cycle
Memory Read Cycle
T1
T2
T3
T4
T5
T6 T7
Content Of Reg H
A0h
Instruction:
A000h MOV A,M
Corresponding Coding: A000h 7E

## Slide 111: Timing Diagram
Instruction:
A000h MOV M,A
Corresponding Coding: A000h 77

## Slide 112: Timing Diagram
Instruction:
A000h MOV M,A
Corresponding Coding: A000h 77
8085
Memory
OFC
MEMW

## Slide 113: Timing Diagram
L Reg
Content of Reg A
A15- A8 (Higher Order Address bus)
00h 7Eh
DA7-DA0 (Lower order address/data Bus)
ALE
RD
WR
IO/M
Op-Code Fetch Cycle
Memory Write Cycle
T1
T2
T3
T4
T5
T6 T7
Content Of Reg H
A0h
Instruction:
A000h MOV M,A
Corresponding Coding: A000h 77

## Slide 114: Chapter 9 Stack and Subroutines

## Slide 115: The Stack
The stack is an area of memory identified by the programmer for temporary storage of information.
The stack is a LIFO structure.
– Last In First Out.
The stack normally grows backwards into memory.
– In other words, the programmer
defines the bottom of the stack and the stack grows up into reducing address range.
Memory
Bottom of the Stack
The Stack grows backwards into memory

## Slide 116: The Stack
Given that the stack grows backwards into memory, it is customary to place the bottom of the stack at the end of memory to keep it as far away from user programs as possible.
In the 8085, the stack is defined by setting the SP (Stack Pointer) register.
LXI SP, FFFFH
This sets the Stack Pointer to location FFFFH (end of memory for the 8085).

## Slide 117: Saving Information on the Stack
Information is saved on the stack by PUSHing it on.
  It is retrieved from the stack by POPing it off.
The 8085 provides two instructions: PUSH and POP for storing information on the stack and retrieving it back.
  Both PUSH and POP work with register pairs ONLY.

## Slide 118: The PUSH Instruction
PUSH B
  Decrement SP
  Copy the contents of register B to the memory location pointed to by SP
location pointed to by SP
– Decrement SP
B
C
SP
FFFD FFFE FFFF
FFFC
FFFB
– Copy the co12ntenFt3s of reg C to the memory
ister
F3
12

## Slide 119: The POP Instruction
POP D
  Copy the contents of the memory location pointed to by the SP to register E
  Increment SP
– Copy the contents of the memory location
o by the S
pointed t P to r er D
– Increment SP
D E
SP
FFFB FFFC FFFD FFFE FFFF
12 F3
egist
F3
12

## Slide 120: Operation of the Stack
During pushing, the stack operates in a “decrement then store” style.
  The stack pointer is decremented first, then the information is placed on the stack.
During poping, the stack operates in a “use then increment” style.
  The information is retrieved from the top of the the stack and then the pointer is incremented.
The SP pointer always points to “the top of the stack”.

## Slide 121: LIFO
The order of PUSHs and POPs must be opposite of each other in order to retrieve information back into its original location.
PUSH B PUSH D
... POP D POP B

## Slide 122: The PSW Register Pair
The 8085 recognizes one additional register pair called the PSW (Program Status Word).
  This register pair is made up of the Accumulator and the Flags registers.
It is possible to push the PSW onto the stack, do whatever operations are needed, then POP it off of the stack.
  The result is that the contents of the Accumulator and the status of the Flags are returned to what they were before the operations were executed.

## Slide 123: Subroutines
A subroutine is a group of instructions that will be used repeatedly in different locations of the program.
  Rather than repeat the same instructions several times, they can be grouped into a subroutine that is called from the different locations.
In Assembly language, a subroutine can exist anywhere in the code.
  However, it is customary to place subroutines separately from the main program.

## Slide 124: Subroutines
The 8085 has two instructions for dealing with subroutines.
  The CALL instruction is used to redirect program execution to the subroutine.
  The RTE insutruction is used to return the execution to the calling routine.

## Slide 125: The CALL Instruction
CALL 4000H
– Push the address of the instruction immediately following the CALL onto the
unter wit
Load the program co h the
t
address supplied with the CALL in
struction.
PC
SP
FFFC FFFD FFFE FFFF
FFFB
2 0 0 3
16-bi
03
20
2000 sCtaALcLk4000
2003–

## Slide 126: The RTE Instruction
RTE
  Retrieve the return address from the top of the stack
  Load the program counter with the return
address.
PC
FFFB FFFC FFFD FFFE FFFF
03
20
2 0 0 3
4014
4015
. . . RTE
SP

## Slide 127: Cautions
The CALL instruction places the return address at the two memory locations immediately before where the Stack Pointer is pointing.
  You must set the SP correctly BEFORE using the CALL instruction.
The RTE instruction takes the contents of the two memory locations at the top of the stack and uses these as the return address.
  Do not modify the stack pointer in a subroutine. You will loose the return address.

## Slide 128: Passing Data to a Subroutine
In Assembly Language data is passed to a subroutine through registers.
  The data is stored in one of the registers by the calling program and the subroutine uses the value from the register.
The other possibility is to use agreed upon memory locations.
  The calling program stores the data in the memory location and the subroutine retrieves the data from the location and uses it.

## Slide 129: Call by Reference and Call by Value
If the subroutine performs operations on the contents of the registers, then these modifications will be transferred back to the calling program upon returning from a subroutine.
  Call by reference
If this is not desired, the subroutine should PUSH all the registers it needs on the stack on entry and POP them on return.
  The original values are restored before execution returns to the calling program.

## Slide 130: Cautions with PUSH and POP
PUSH and POP should be used in opposite order.
There has to be as many POP’s as there are PUSH’s.
– If not, the RET statement will pick up the wrong information from the top of the stack and the program will fail.
It is not advisable to place PUSH or POP inside a loop.

## Slide 131: Conditional CALL and RTE Instructions
The 8085 supports conditional CALL and conditional RTE instructions.
  The same conditions used with conditional JUMP instructions can be used.
  CC, call subroutine if Carry flag is set.
  CNC, call subroutine if Carry flag is not set
  RC, return from subroutine if Carry flag is set
  RNC, return from subroutine if Carry flag is not set
  Etc.

## Slide 132: A Proper Subroutine
According to Software Engineering practices, a proper subroutine:
  Is only entered with a CALL and exited with an RTE
  Has a single entry point
    Do not use a CALL statement to jump into different points of the same subroutine.
  Has a single exit point
    There should be one return statement from any subroutine.
Following these rules, there should not be any confusion with PUSH and POP usage.

## Slide 134: The Design and Operation of Memory
Memory in a microprocessor system is where information (data and instructions) is kept. It can be classified into two main types:
Main memory (RAM and ROM)
Storage memory (Disks , CD ROMs, etc.)
The simple view of RAM is that it is made up of registers that are made up of flip-flops (or memory elements).
The number of flip-flops in a “memory register” determines the size of the memory word.
ROM on the other hand uses diodes instead of the flip-flops to permanently hold the information.
1

## Slide 135: Accessing Information in Memory
For the microprocessor to access (Read or Write) information in memory (RAM or ROM), it needs to do the following:
Select the right memory chip (using part of the address bus).
Identify the memory location (using the rest of the address bus).
Access the data (using the data bus).
2

## Slide 136: Tri-State Buffers
An important circuit element that is used extensively in memory.
This buffer is a logic circuit that has three states:
Logic 0, logic1, and high impedance.
When this circuit is in high impedance mode it looks as if it is disconnected from the output completely.
The Output is Low
3
The Output is High
High Impedance

## Slide 137: The Tri-State Buffer
4
This circuit has two inputs and one output.
The first input behaves like the normal input for the circuit.
The second input is an “enable”.
If it is set high, the output follows the proper circuit behavior.
If it is set low, the output looks like a wire connected to nothing.
Input Output
Enable
Input
Output
Enable
OR

## Slide 138: The Basic Memory Element
The basic memory element is similar to a D latch.
This latch has an input where the data comes in. It has an enable input and an output on which data comes out.
5
Dat
Data Output
a Input | D Q EN | 
Enable |  | 

## Slide 139: The Basic Memory Element
However, this is not safe.
Data is always present on the input and the output is always set to the contents of the latch.
To avoid this, tri-state buffers are added at the input and output of the latch.
Q
D
Data Input Data Output
Enable
EN
WR
RD
6

## Slide 140: The Basic Memory Element
The WR signal controls the input buffer.
The bar over WR means that this is an active low signal.
So, if WR is 0 the input data reaches the latch input.
If WR is 1 the input of the latch looks like a wire connected to nothing.
The RD signal controls the output in a similar manner.
7

## Slide 141: A Memory “Register”
RD
EN
Q
D
EN
Q
D
EN
Q
D
EN
Q
D
EN
If we take four of these latches and connect them together, we would have a 4-bit memory register
I0 I1 I2 I3
WR
8
O0
O1
O2
O3

## Slide 142: A group of memory registers
9
Expanding on this scheme to add more memory registers we get the diagram to the right.
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D Q
EN
D0
D1
D2
D3
D0
D1
D2
D3
o
o
o
o
o
o
o
o
WR
RD

## Slide 143: Externally Initiated Operations
External devices can initiate (start) one of the 4 following operations:
Reset
All operations are stopped and the program counter is reset to 0000.
Interrupt
The microprocessor’s operations are interrupted and the microprocessor executes what is called a “service routine”.
This routine “handles” the interrupt, (perform the necessary operations). Then the microprocessor returns to its previous operations and continues.

## Slide 144: A group of Memory Registers
 | Input Buffers |  |  |  | 
 | Memory Reg. 0 |  |  |  | 
 | Memory Reg. 1 |  |  |  | 
 | Memory Reg. 2 |  |  |  | 
 | Memory Reg. 3 |  |  |  | 
 | Output Buffers |  |  |  | 
If we represent each memory location (Register) as a block we get the following
I0 I1 I2 I3
WR
EN0 EN1 EN2 EN3
RD
O0 O1 O2 O3

## Slide 145: The Design of a Memory Chip
Using the RD and WR controls we can determine the direction of flow either into or out of memory. Then using the appropriate Enable input we enable an individual memory register.
What we have just designed is a memory with 4 locations and each location has 4 elements (bits). This memory would be called 4 X 4 [Number of location X number of bits per location].

## Slide 146: The Enable Inputs
How do we produce these enable line?
Since we can never have more than one of these enables active at the same time, we can have them encoded to reduce the number of lines coming into the chip.
These encoded lines are the address lines for memory.

## Slide 147: The Design of a Memory Chip
So, the previous diagram would now look like the
following:
Input Buffers
Output Buffers
Memory Reg. 0
Memory Reg. 1
Memory Reg. 2
Memory Reg. 3
I0 I1 I2 I3
O0 O1 O2 O3
WR
RD
r
A D
d e
d c
o
e d
s e
s r
A1
A
0

## Slide 148: The Design of a Memory Chip
Since we have tri-state buffers on both the inputs and outputs of the flip flops, we can actually use
o
ne set of pins only.
The chip would now look li
Input Buffers
Output Buffers
Memory Reg. 0
Memory Reg. 1
Memory Reg. 2
Memory Reg. 3
WR
RD
A
d
d
r
e
s
s
D
e
c
o
d
e
r
A1
A
0
keDt0his:
D1
D2
D
3
D0
D1 D2
D
3
A1
A
0
RD WR

## Slide 149: The steps of writing into Memory
What happens when the programmer issues the STA instruction?
The microprocessor would turn on the WR control (WR = 0) and turn off the RD control (RD = 1).
The address is applied to the address decoder which generates a single Enable signal to turn on only one of the memory registers.
The data is then applied on the data lines and it is stored into the enabled register.

## Slide 150: Dimensions of Memory
17
Memory is usually measured by two numbers: its length and its width (Length X Width).
The length is the total number of locations.
The width is the number of bits in each location.
The length (total number of locations) is a function of the number of address lines.
# of memory locations = 2( # of address lines)
So, a memory chip with 10 address lines would have
210 = 1024 locations (1K)
Looking at it from the other side, a memory chip with 4K locations would need
Log2 4096=12 address lines

## Slide 151: The 8085 and Memory
The 8085 has 16 address lines. That means it can address
216 = 64K memory locations.
Then it will need 1 memory chip with 64 k locations, or 2 chips with 32 K in each, or 4 with 16 K each or 16 of the 4 K chips, etc.
how would we use these address lines to control the multiple chips?

## Slide 152: Chip Select
Usually, each memory chip has a CS (Chip Select) input. The chip will only work if an active signal is applied on that input.
To allow the use of multiple chips in the make up of memory, we need to use a number of the address lines for the purpose of “chip selection”.
These address lines are decoded to generate the 2n necessary CS inputs for the memory chips to be used.

## Slide 153: Chip Selection Example
Assume that we need to build a memory system made up of 4 of the 4 X 4 memory chips we designed earlier.
We will need to use 2 inputs and a decoder to identify which chip will be used at what time.
The resulting design would now look like the one on the following slide.

## Slide 154: Chip Selection Example
RD WR
A0 A1
CS
RD WR
A0 A1
CS
RD WR
A0 A1
CS
RD WR
A0 A1
CS
2 X4
Decoder
A3
A2
A0 A1
RD
WR
D0 D1

## Slide 155: Memory Map and Addresses
FFFF
Address Range
EPROM
RAM 1
RAM 2
RAM 3
RAM 4
The memory map is a picture representation of the address range and shows where the different memory chips are located within the address range.
0000 0000
8FFF
9000
A3FF A400
Address Range of EPROM Chip
3FFF
4400
Address Range of 1st RAM Chip
5FFF
6000
Address Range of 2nd RAM Chip
Address Range of 3rd RAM Chip
Address Range of 4th RAM Chip
F7FF

## Slide 156: Address Range of a Memory Chip
The address range of a particular chip is the list of all addresses that are mapped to the chip.
An example for the address range and its relationship to the memory chips would be the Post Office Boxes in the post office.
Each box has its unique number that is assigned sequentially. (memory locations)
The boxes are grouped into groups. (memory chips)
The first box in a group has the number immediately after the last box in the previous group.

## Slide 157: Address Range of a Memory Chip
The above example can be modified slightly to make it closer to our discussion on memory.
Let’s say that this post office has only 1000 boxes.
Let’s also say that these are grouped into 10 groups of 100 boxes each. Boxes 0000 to 0099 are in group 0, boxes 0100 to 0199 are in group 1 and so on.
We can look at the box number as if it is made up of two pieces:
The group number and the box’s index within the group.
So, box number 436 is the 36th box in the 4th group.
The upper digit of the box number identifies the group and the lower two digits identify the box within the group.

## Slide 158: The 8085 and Address Ranges
The 8085 has 16 address lines. So, it can address a total of 64K memory locations.
If we use memory chips with 1K locations each, then we will need 64 such chips.
The 1K memory chip needs 10 address lines to uniquely identify the 1K locations. (log21024 = 10)
That leaves 6 address lines which is the exact number needed for selecting between the 64 different chips (log264 = 6).

## Slide 159: The 8085 and Address Ranges
Depending on the combination on the address lines A15 - A10 , the address range of the specified chip is determined.
Now, we can break up the 16-bit address of the 8085 into two pieces:
Chip Selection Location Selection within the Chip
A15 A14 A13 A12 A11 A10 A9 A8 A7 A6 A5 A4 A3 A2 A1 A0

## Slide 160: Chip Select Example
A chip that uses the combination A15 - A10 = 001000 would have addresses that range from 2000H to 23FFH.
Keep in mind that the 10 address lines on the chip gives a range of 00 0000 0000 to 11 1111 1111 or 000H to 3FFH for each of the chips.
The memory chip in this example would require the following circuit on its chip select input:
CS
A10
A11
A12
A13
A14
A15

## Slide 161: Chip Select Example
If we change the above combination to the following:
Now the chip would have addresses ranging from: 2400 to 27FF.
Changing the combination of the address bits connected to the chip select changes the address range for the memory chip.
CS
A10
A11
A12
A13
A14
A15

## Slide 162: Chip Select Example
To illustrate this with a picture:
in the first case, the memory chip occupies the piece of the memory map identified as before.
In the second case, it occupies the piece identified as
after.
0000
2000
23FF
FFFF
0000
2400
27FF
FFFF
Before After

## Slide 163: High-Order vs. Low-Order Address Lines
The address lines from a microprocessor can be classified into two types:
High-Order
Used for memory chip selection
Low-Order
Used for location selection within a memory chip.
This classification is highly dependent on the memory system design.

## Slide 164: Data Lines
All of the above discussion has been regarding memory length. Lets look at memory width.
We said that the width is the number of bits in each memory word.
We have been assuming so far that our memory chips have the right width.
What if they don’t?
It is very common to find memory chips that have only 4 bits per location. How would you design a byte wide memory system using these chips?
We use two chips for the same address range. One chip will supply 4 of the data bits per address and the other chip supply the other 4 data bits for the same address.

## Slide 165: Data Lines
CS
A0
… A9
CS
CS
D0
… D3
D4
… D7

## Slide 166: Interrupts

## Slide 167: Interrupts
Interrupt is a process where an external device can get the attention of the microprocessor.
  The process starts from the I/O device
  The process is asynchronous.
Interrupts can be classified into two types:
Maskable (can be delayed)
Non-Maskable (can not be delayed)
Interrupts can also be classified into:
  Vectored (the address of the service routine is hard-wired)
  Non-vectored (the address of the service routine needs to be supplied externally)

## Slide 168: Interrupts
An interrupt is considered to be an emergency signal.
  The Microprocessor should respond to it as soon as possible.
When the Microprocessor receives an interrupt signal, it suspends the currently executing program and jumps to an Interrupt Service Routine (ISR) to respond to the incoming interrupt.
  Each interrupt will most probably have its own ISR.

## Slide 169: Responding to Interrupts
Responding to an interrupt may be immediate or delayed depending on whether the interrupt is maskable or non-maskable and whether interrupts are being masked or not.
There are two ways of redirecting the execution to the ISR depending on whether the interrupt is vectored or non-vectored.
  The vector is already known to the Microprocessor
  The device will have to supply the vector to the Microprocessor

## Slide 170: The 8085 Interrupts
The maskable interrupt process in the 8085 is controlled by a single flip flop inside the microprocessor. This Interrupt Enable flip flop is controlled using the two instructions “EI” and “DI”.
The 8085 has a single Non-Maskable interrupt.
– The non-maskable interrupt is not affected by the value of the Interrupt Enable flip flop.

## Slide 171: The 8085 Interrupts
The 8085 has 5 interrupt inputs.
  The INTR input.
    The INTR input is the only non-vectored interrupt.
    INTR is maskable using the EI/DI instruction pair.
  RST 5.5, RST 6.5, RST 7.5 are all automatically vectored.
    RST 5.5, RST 6.5, and RST 7.5 are all maskable.
  TRAP is the only non-maskable interrupt in the 8085
    TRAP is also automatically vectored

## Slide 172: The 8085 Interrupts
Interrupt name | Maskable | Vectored
INTR | Yes | No
RST 5.5 | Yes | Yes
RST 6.5 | Yes | Yes
RST 7.5 | Yes | Yes
TRAP | No | Yes

## Slide 173: Interrupt Vectors and the Vector Table
An interrupt vector is a pointer to where the ISR is stored in memory.
All interrupts (vectored or otherwise) are mapped onto a memory area called the Interrupt Vector Table (IVT).
  The IVT is usually located in memory page 00 (0000H
- 00FFH).
  The purpose of the IVT is to hold the vectors that redirect the microprocessor to the right place when an interrupt arrives.
  The IVT is divided into several blocks. Each block is used by one of the interrupts to hold its “vector”

## Slide 174: The 8085 Non-Vectored Interrupt Process
The interrupt process should be enabled using the EI instruction.
The 8085 checks for an interrupt during the execution of every instruction.
If there is an interrupt, the microprocessor will complete the executing instruction, and start a RESTART sequence.
The RESTART sequence resets the interrupt flip flop and activates the interrupt acknowledge signal (INTA).
Upon receiving the INTA signal, the interrupting device is expected to return the op-code of one of the 8 RST instructions.

## Slide 175: The 8085 Non-Vectored Interrupt Process
When the microprocessor executes the RST instruction received from the device, it saves the address of the next instruction on the stack and jumps to the appropriate entry in the IVT.
The IVT entry must redirect the microprocessor to the actual service routine.
The service routine must include the instruction EI to re-enable the interrupt process.
At the end of the service routine, the RET instruction returns the execution to where the program was interrupted.

## Slide 176: The 8085 Non-Vectored Interrupt Process
The 8085 recognizes 8 RESTART instructions: RST0 - RST7.
– each of these would send the execution to a predetermined hard-wired memory location:
Restart Instruction | Equivalent to
RST0 | CALL 0000H
RST1 | CALL 0008H
RST2 | CALL 0010H
RST3 | CALL 0018H
RST4 | CALL 0020H
RST5 | CALL 0028H
RST6 | CALL 0030H
RST7 | CALL 0038H

## Slide 177: Restart Sequence
The restart sequence is made up of three machine cycles
  In the 1st machine cycle:
    The microprocessor sends the INTA signal.
    While INTA is active the microprocessor reads the data lines expecting to receive, from the interrupting device, the opcode for the specific RST instruction.
  In the 2nd and 3rd machine cycles:
    the 16-bit address of the next instruction is saved on the stack.
    Then the microprocessor jumps to the address associated with the specified RST instruction.

## Slide 178: Restart Sequence
The location in the IVT associated with the RST instruction can not hold the complete service routine.
  The routine is written somewhere else in memory.
  Only a JUMP instruction to the ISR’s location is kept in the IVT block.

## Slide 179: Hardware Generation of RST Opcode
How does the external device produce the opcode for the appropriate RST instruction?
  The opcode is simply a collection of bits.
  So, the device needs to set the bits of the data bus to the appropriate value in response to an INTA signal.

## Slide 180: Hardware Generation of RST
The following is an
example of generating RST 5:
RST 5’s opcode is EF =
D D
76543210
11101111
Opcode

## Slide 181: Hardware Generation of RST Opcode
During the interrupt acknowledge machine cycle, (the 1st machine cycle of the RST operation):
  The Microprocessor activates the INTA signal.
  This signal will enable the Tri-state buffers, which will place the value EFH on the data bus.
  Therefore, sending the Microprocessor the RST 5 instruction.
The RST 5 instruction is exactly equivalent to CALL 0028H

## Slide 182: Issues in Implementing INTR Interrupts
How long must INTR remain high?
  The microprocessor checks the INTR line one clock cycle before the last T-state of each instruction.
  The interrupt process is Asynchronous.
  The INTR must remain active long enough to allow for the longest instruction.
  The longest instruction for the 8085 is the conditional CALL instruction which requires 18 T-states.
Therefore, the INTR must remain active for 17.5
T-states.

## Slide 183: Issues in Implementing INTR Interrupts
How long can the INTR remain high?
  The INTR line must be deactivated before the EI is executed. Otherwise, the microprocessor will be interrupted again.
  The worst case situation is when EI is the first instruction in the ISR.
  Once the microprocessor starts to respond to an INTR interrupt, INTA becomes active (=0).
Therefore, INTR should be turned off as soon as the INTA signal is received.

## Slide 184: Issues in Implementing INTR Interrupts
Can the microprocessor be interrupted again before the completion of the ISR?
  As soon as the 1st interrupt arrives, all maskable interrupts are disabled.
  They will only be enabled after the execution of the EI instruction.
Therefore, the answer is: “only if you allow it to”.
If the EI instruction is placed early in the ISR, other interrupt may occur before the ISR is done.

## Slide 185: Multiple Interrupts & Priorities
How do we allow multiple devices to interrupt using the INTR line?
  The microprocessor can only respond to one signal on INTR at a time.
  Therefore, we must allow the signal from only one of the devices to reach the microprocessor.
  We must assign some priority to the different devices and allow their signals to reach the microprocessor according to the priority.

## Slide 186: The Priority Encoder
The solution is to use a circuit called the priority encoder (74366).
  This circuit has 8 inputs and 3 outputs.
  The inputs are assigned increasing priorities according to the increasing index of the input.
    Input 7 has highest priority and input 0 has the lowest.
  The 3 outputs carry the index of the highest priority active input.
  Figure 12.4 in the book shoes how this circuit can be used with a Tri-state buffer to implement an interrupt priority scheme.
    The figure in the textbook does not show the method for distributing the INTA signal back to the individual devices.

## Slide 187: Multiple Interrupts & Priorities
Note that the opcodes for the different RST instructions follow a set pattern.
  Bit D5, D4 and D3 of the opcodes change in a binary sequence from RST 7 down to RST 0.
  The other bits are always 1.
  This allows the code generated by the 74366 to be used directly to choose the appropriate RST instruction.
The one draw back to this scheme is that the only way to change the priority of the devices connected to the 74366 is to reconnect the hardware.

## Slide 188: Multiple Interrupts and Priority
Dev. 7
Dev. 6
Dev. 5
Dev. 4
Dev. 3
Dev. 2
Dev. 1
Dev. 0
7
4
1
3
8
INTA INTR
8
AD7
AD6 0
AD5
AD4 8
AD3
AD2 5
AD1 AD0
O7 O6 O5 O4 O3 O2 O1 O0
I7
I6 7
I5 4
I4
I3 3
I2 6
I1
I0 6
Tri – State
Buffer
Priority
Encoder
+5 V
INTR Circuit INTA Circuit
RST Circuit

## Slide 189: The 8085 Maskable/Vectored Interrupts
The 8085 has 4 Masked/Vectored interrupt inputs.
– RST 5.5, RST 6.5, RST 7.5
  They are all maskable.
  They are automatically vectored according to the following table:
– The vectors for these interrupt fall in between the vectors for the RST instructions. That’s why they have names like RST 5.5 (RST 5 and a half).
Interrupt | Vector
RST 5.5 | 002CH
RST 6.5 | 0034H
RST 7.5 | 003CH

## Slide 190: Masking RST 5.5, RST 6.5 and RST 7.5
These three interrupts are masked at two levels:
  Through the Interrupt Enable flip flop and the EI/DI instructions.
    The Interrupt Enable flip flop controls the whole maskable interrupt process.
  Through individual mask flip flops that control the availability of the individual interrupts.
    These flip flops control the interrupts individually.

## Slide 191: Maskable Interrupts
Interrupt Enable Flip Flop
INTR
RST 5.5
RST 6.5
M 5.5
M 6.5
M 7.5
RST7.5 Memory
RST 7.5

## Slide 192: The 8085 Maskable/Vectored Interrupt Process
The interrupt process should be enabled using the EI instruction.
The 8085 checks for an interrupt during the execution of every instruction.
If there is an interrupt, and if the interrupt is enabled using the interrupt mask, the microprocessor will complete the executing instruction, and reset the interrupt flip flop.
The microprocessor then executes a call instruction that sends the execution to the appropriate location in the interrupt vector table.

## Slide 193: The 8085 Maskable/Vectored Interrupt Process
When the microprocessor executes the call instruction, it saves the address of the next instruction on the stack.
The microprocessor jumps to the specific service routine.
The service routine must include the instruction EI to re-enable the interrupt process.
At the end of the service routine, the RET instruction returns the execution to where the program was interrupted.

## Slide 194: Manipulating the Masks
The Interrupt Enable flip flop is manipulated using the EI/DI instructions.
The individual masks for RST 5.5, RST 6.5 and RST 7.5 are manipulated using the SIM instruction.
– This instruction takes the bit pattern in the Accumulator and applies it to the interrupt mask enabling and disabling the specific interrupts.

## Slide 195: How SIM Interprets the Accumulator 7 6 5 4 3 2 1 0
SDO
SDE
XXX R7.5 MSE M7.5 M6.5 M5.5
RST5.5 Mask RST6.5 Mask RST7.5 Mask
}
- Available
- Masked
Mask Set Enable 0 - Ignore bits 0-2
1 - Set the masks according to bits 0-2
Force RST7.5 Flip Flop to reset
Not Used
Enable Serial Data 0 - Ignore bit 7
1 - Send bit 7 to SOD pin
Serial Data Out

## Slide 196: SIM and the Interrupt Mask
Bit 0 is the mask for RST 5.5, bit 1 is the mask for RST 6.5 and bit 2 is the mask for RST 7.5.
  If the mask bit is 0, the interrupt is available.
  If the mask bit is 1, the interrupt is masked.
Bit 3 (Mask Set Enable - MSE) is an enable for setting the mask.
  If it is set to 0 the mask is ignored and the old settings remain.
  If it is set to 1, the new setting are applied.
  The SIM instruction is used for multiple purposes and not only for setting interrupt masks.
    It is also used to control functionality such as Serial Data Transmission.
    Therefore, bit 3 is necessary to tell the microprocessor whether or not the interrupt masks should be modified

## Slide 197: SIM and the Interrupt Mask
The RST 7.5 interrupt is the only 8085 interrupt that has memory.
  If a signal on RST7.5 arrives while it is masked, a flip flop will remember the signal.
  When RST7.5 is unmasked, the microprocessor will be interrupted even if the device has removed the interrupt signal.
  This flip flop will be automatically reset when the microprocessor responds to an RST 7.5 interrupt.
Bit 4 of the accumulator in the SIM instruction allows explicitly resetting the RST 7.5 memory even if the microprocessor did not respond to it.

## Slide 198: SIM and the Interrupt Mask
The SIM instruction can also be used to perform serial data transmission out of the 8085’s SOD pin.
– One bit at a time can be sent out serially over the SOD pin.
Bit 6 is used to tell the microprocessor whether or not to perform serial data transmission
  If 0, then do not perform serial data transmission
  If 1, then do.
The value to be sent out on SOD has to be placed in bit 7 of the accumulator.
Bit 5 is not used by the SIM instruction

## Slide 199: Using the SIM Instruction to Modify the Interrupt Masks
Example: Set the interrupt masks so that RST5.5 is enabled, RST6.5 is masked, and RST7.5 is enabled.
– First, determine the contents of the accumulator
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
SDO
SDE XXX
R7.5 MSE M7.5 M6.5 M5.5
Enable 5.5
Disable 6.5
Enable 7.5
Allow setting the masks
Don’t reset the flip flop
Bit 5 is not used
Don’t use serial data
Serial data is ignored
bit 0 = 0
bit 1 = 1
bit 2 = 0
bit 3 = 1
bit 4 = 0
bit 5 = 0
bit 6 = 0
bit 7 = 0
Contents of accumulator are: 0AH
EI
MVI A, 0A SIM
; Enable interrupts including INTR
; Prepare the mask to enable RST 7.5, and 5.5, disable 6.5
; Apply the settings RST masks

## Slide 200: Triggering Levels
RST 7.5 is positive edge sensitive.
  When a positive edge appears on the RST7.5 line, a logic 1 is stored in the flip-flop as a “pending” interrupt.
  Since the value has been stored in the flip flop, the line does not have to be high when the microprocessor checks for the interrupt to be recognized.
  The line must go to zero and back to one before a new interrupt is recognized.
RST 6.5 and RST 5.5 are level sensitive.
  The interrupting signal must remain present until the microprocessor checks for interrupts.

## Slide 201: Determining the Current Mask Settings
RIM instruction: Read Interrupt Mask
– Load the accumulator with an 8-bit pattern showing the status of each interrupt pin and mask.
RST 5.5
RST 6.5
M 5.5
Interrupt Enable Flip Flop
M 6.5
RST7.5 Memory
RST 7.5
M 7.5
SDI
P7.5
P6.5 P5.5 IE M7.5 M6.5 M5.5
7 6 5 4 3 2 1 0

## Slide 202: How RIM sets the Accumulator’s different bits
SDI | P7.5 | P6.5 | P5.5 | IE | M7.5 | M6.5 | M5.5
7 6 5 4 3 2 1 0
RST5.5 Mask
RST6.5 Mask
RST7.5 Mask
}
- Available
- Masked
Interrupt Enable
Value of the Interrupt Enable Flip Flop
Serial Data In
RST5.5 Interrupt Pending RST6.5 Interrupt Pending RST7.5 Interrupt Pending

## Slide 203: The RIM Instruction and the Masks
Bits 0-2 show the current setting of the mask for each of RST 7.5, RST 6.5 and RST 5.5
  They return the contents of the three mask flip flops.
  They can be used by a program to read the mask settings in order to modify only the right mask.
Bit 3 shows whether the maskable interrupt process is enabled or not.
  It returns the contents of the Interrupt Enable Flip Flop.
  It can be used by a program to determine whether or not interrupts are enabled.

## Slide 204: The RIM Instruction and the Masks
Bits 4-6 show whether or not there are pending interrupts on RST 7.5, RST 6.5, and RST 5.5
  Bits 4 and 5 return the current value of the RST5.5 and RST6.5 pins.
  Bit 6 returns the current value of the RST7.5 memory flip flop.
Bit 7 is used for Serial Data Input.
  The RIM instruction reads the value of the SID pin on the microprocessor and returns it in this bit.

## Slide 205: Pending Interrupts
Since the 8085 has five interrupt lines, interrupts may occur during an ISR and remain pending.
  Using the RIM instruction, the programmer can read the status of the interrupt lines and find if there are any pending interrupts.
  The advantage is being able to find about interrupts on RST 7.5, RST 6.5, and RST 5.5 without having to enable low level interrupts like INTR.

## Slide 206: Using RIM and SIM to set Individual Masks
Example: Set the mask to enable RST6.5 without modifying the masks for RST5.5 and RST7.5.
  In order to do this correctly, we need to use the RIM instruction to find the current settings of the RST5.5 and RST7.5 masks.
  Then we can use the SIM instruction to set the masks using this information.
  Given that both RIM and SIM use the Accumulator, we can use some logical operations to masks the un-needed values returned by RIM and turn them into the values needed by SIM.

## Slide 207: Using RIM and SIM to set Individual Masks
SDO
SDE XXX
R7.5 MSE M7.5 M6.5 M5.5
0
0
0
0
0
0
0
1
– Assume the RST5.5 and RST7.5 are enabled and the interrupt process
is disabled.
RIM
; Read the current settings.
ORI 08H
; 0 0 0 0 1 0 0 0
; Set bit 4 for MSE.
ANI 0DH
; 0 0 0 0 1 1 0 1
; Turn off Serial Data, Don’t reset
; RST7.5 flip flop, and set the mask
; for RST6.5 off. Don’t cares are
; assumed to be 0.
SIM
; Apply the settings.
Accumulator
SDI
P7.5 P6.5
P5.5 IE M7.5 M6.5 M5.5
0 0 0 0 0 0 1 0
1 0
0 0 0 0
1 0
0 0 0 0 1 0 0 0

## Slide 208: TRAP
TRAP is the only non-maskable interrupt.
  It does not need to be enabled because it cannot be disabled.
It has the highest priority amongst interrupts.
It is edge and level sensitive.
  It needs to be high and stay high to be recognized.
  Once it is recognized, it won’t be recognized again until it goes low, then high again.
TRAP is usually used for power failure and emergency shutoff.

## Slide 209: Internal Interrupt Priority
Internally, the 8085 implements an interrupt priority scheme.
  The interrupts are ordered as follows:
    TRAP
    RST 7.5
    RST 6.5
    RST 5.5
    INTR
  However, TRAP has lower priority than the HLD signal used for DMA.

## Slide 210: The 8085 Interrupts
Interrupt Name | Maskable | Masking Method | Vectored | Memory | Triggerin g Method
INTR | Yes | DI / EI | No | No | Level Sensitive
RST 5.5 / RST 6.5 | Yes | DI / EI SIM | Yes | No | Level Sensitive
RST 7.5 | Yes | DI / EI SIM | Yes | Yes | Edge Sensitive
TRAP | No | None | Yes | No | Level & Edge Sensitive

## Slide 211: Additional Concepts and Processes
Programmable Interrupt Controller 8259 A
  A programmable interrupt managing device
    It manages 8 interrupt requests.
    It can vector an interrupt anywhere in memory without additional H/W.
    It can support 8 levels of interrupt priorities.
    The priority scheme can be extended to 64 levels using a hierarchy 0f 8259 device.

## Slide 212: The Need for the 8259A
The 8085 INTR interrupt scheme presented earlier has a few limitations:
  The RST instructions are all vectored to memory page 00H, which is usually used for ROM.
  It requires additional hardware to produce the RST instruction opcodes.
  Priorities are set by hardware.
Therefore, we need a device like the 8259A to expand the priority scheme and allow mapping to pages other than 00H.

## Slide 213: Interfacing the 8259A to the 8085
Dev. 7
Dev. 6
Dev. 5
Dev. 4
Dev. 3
Dev. 2
Dev. 1
Dev. 0
8
2
5
9
A
8
0
8
5
INTA
INTR
AD7 AD6 AD5 AD4 AD3 AD2
AD1 AD0
I7 I6 I5 I4
3
I I
2
I1
I0

## Slide 214: Operating of the 8259A
The 8259A requires the microprocessor to provide 2 control words to set up its operation. After that, the following sequence occurs:
  One or more interrupts come in.
  The 8259A resolves the interrupt priorities based on its internal settings
  The 8259A sends an INTR signal to the microprocessor.
  The microprocessor responds with an INTA signal and turns off the interrupt enable flip flop.
  The 8259A responds by placing the op-code for the CALL instruction (CDH) on the data bus.

## Slide 215: Operating of the 8259A
When the microprocessor receives the op-code for CALL instead of RST, it recognizes that the device will be sending 16 more bits for the address.
The microprocessor sends a second INTA signal.
The 8259A sends the high order byte of the ISR’s address.
The microprocessor sends a third INTA signal.
The 8259A sends the low order byte of the ISR’s address.
The microprocessor executes the CALL instruction and jumps to the ISR.

## Slide 216: Direct Memory Access
This is a process where data is transferred between two peripherals directly without the involvement of the microprocessor.
  This process employs the HOLD pin on the microprocessor
    The external DMA controller sends a signal on the HOLD pin to the microprocessor.
    The microprocessor completes the current operation and sends a signal on HLDA and stops using the buses.
    Once the DMA controller is done, it turns off the HOLD signal and the microprocessor takes back control of the buses.

## Slide 217: Serial I/O and Data Communication

## Slide 218: Basic Concepts in Serial I/O
Interfacing requirements:
  Identify the device through a port number.
    Memory-mapped.
    Peripheral-mapped.
  Enable the device using the Read and Write control signals.
    Read for an input device.
    Write for an output device.
  Only one data line is used to transfer the information instead of the entire data bus.

## Slide 219: Basic Concepts in Serial I/O
Controlling the transfer of data:
  Microprocessor control.
    Unconditional, polling, status check, etc.
  Device control.
    Interrupt.

## Slide 220: Synchronous Data Transmission
The transmitter and receiver are synchronized.
– A sequence of synchronization signals is sent before the communication begins.
Usually used for high speed transmission.
  More than 20 K bits/sec.
Message based.
– Synchronization occurs at the beginning of a long message.

## Slide 221: Asynchronous Data Transmission
Transmission occurs at any time.
Character based.
  Each character is sent separately.
Generally used for low speed transmission.
  Less the 20 K bits/sec.

## Slide 222: Asynchronous Data Transmission
Follows agreed upon standards:
  The line is normally at logic one (mark).
    Logic 0 is known as space.
  The transmission begins with a start bit (low).
  Then the seven or eight bits representing the character are transmitted.
  The transmission is concluded with one or two stop bits.
art
 | St | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | St | op | 
Time
One Character

## Slide 223: Simplex and Duplex Transmission
Simplex.
  One-way transmission.
  Only one wire is needed to connect the two devices
  Like communication from computer to a printer.
Half-Duplex.
  Two-way transmission but one way at a time.
  One wire is sufficient.
Full-Duplex.
  Data flows both ways at the same time.
  Two wires are needed.
  Like transmission between two computers.

## Slide 224: Rate of Transmission
For parallel transmission, all of the bits are sent at once.
For serial transmission, the bits are sent one at a time.
– Therefore, there needs to be agreement on how “long” each bit stays on the line.
The rate of transmission is usually measured in bits/second or baud.

## Slide 225: Length of Each Bit
Given a certain baud rate, how long should each bit last?
  Baud = bits / second.
  Seconds / bits = 1 /baud.
  At 1200 baud, a bit lasts 1/1200 = 0.83 m Sec.

## Slide 226: Transmitting a Character
To send the character A over a serial communication line at a baud rate of 56.6 K:
  ASCII for A is 41H = 01000001.
  Must add a start bit and two stop bits:
    11 01000001 0
  Each bit should last 1/56.6K = 17.66  Sec.
    Known as bit time.
  Set up a delay loop for 17.66  Sec and set the transmission line to the different bits for the duration of the loop.

## Slide 227: Error Checking
Various types of errors may occur during transmission.
  To allow checking for these errors, additional information is transmitted with the data.
Error checking techniques:
  Parity Checking.
  Checksum.
These techniques are for error checking not correction.
  They only indicate that an error has occurred.
  They do not indicate where or what the correct information is.

## Slide 228: Parity Checking
Make the number of 1’s in the data Odd or Even.
  Given that ASCII is a 7-bit code, bit D7 is used to carry the parity information.
  Even Parity
    The transmitter counts the number of ones in the data. If there is an odd number of 1’s, bit D7 is set to 1 to make the total number of 1’s even.
    The receiver calculates the parity of the received message, it should match bit D7.
– If it doesn’t match, there was an error in the transmission.

## Slide 229: Checksum
Used when larger blocks of data are being transmitted.
The transmitter adds all of the bytes in the message without carries. It then calculates the 2’s complement of the result and send that as the last byte.
The receiver adds all of the bytes in the message including the last byte. The result should be 0.
– If it isn’t an error has occurred.

## Slide 230: RS 232
A communication standard for connecting computers to printers, modems, etc.
  The most common communication standard.
  Defined in the 1950’s.
  It uses voltages between +15 and –15 V.
  Restricted to speeds less than 20 K baud.
  Restricted to distances of less than 50 feet (15 m).
The original standard uses 25 wires to connect the two devices.
  However, in reality only three of these wires are needed.

## Slide 231: Software-Controlled Serial Transmission
The main steps involved in serially transmitting a character are:
  Transmission line is at logic 1 by default.
  Transmit a start bit for one complete bit length.
  Transmit the character as a stream of bits with appropriate delay.
  Calculate parity and transmit it if needed.
  Transmit the appropriate number of stop bits.
  Transmission line returns to logic 1.

## Slide 232: Serial Transmission
0
1
0
0
0
0
0
1
D7 D6 D5 D4 D3 D2 D1 D0
Accumulator
Shift
Output Port
0 1 0 0 0 0 0 1
Start
Stop
Time
D0

## Slide 233: Flowchart of Serial Transmission
Set up Bit Counter
Set bit D0 of A to 0 (Start Bit)
Wait Bit Time
Get character into A
Wait Bit Time
Rotate A Left Decrement Bit Counter
Add Parity Send Stop Bit(s)
No
Last Bit?
Yes

## Slide 234: Software-Controlled Serial Reception
The main steps involved in serial reception are:
  Wait for a low to appear on the transmission line.
    Start bit
  Read the value of the line over the next 8 bit lengths.
    The 8 bits of the character.
  Calculate parity and compare it to bit 8 of the character.
    Only if parity checking is being used.
  Verify the reception of the appropriate number of stop bits.

## Slide 235: Serial Reception
D7
D6
0 D5
0 D4
0 D3
0 D2
D1
D0
Accumulator
Shift
0 1 0 0 0 0 0 1
Start
Stop
Time
D7
Input Port

## Slide 236: Flowchart of Serial Reception
Read Input Port
Start Bit?
Yes
No
Wait for Half Bit Time
Bit Still Low?
Yes
No
Start Bit Counter
Wait Bit Time Read Input Port
Decrement Counter
Last Bit?
Check Parity Wait for Stop Bits
Yes
No

## Slide 237: The 8085 Serial I/O Lines
The 8085 Microprocessor has two serial I/O pins:
  SOD – Serial Output Data
  SID – Serial Input Data
Serial input and output is controlled using the RIM and SIM instructions respectively.

## Slide 238: SIM and Serial Output
As was discussed in Chapter 12, the SIM instruction has dual use.
  It is used for controlling the maskable interrupt process
  For the serial output process.
The figure below shows how SIM uses the accumulator for Serial Output.
SDO
SDE
XXX R7.5 MSE M7.5 M6.5 M5.5
7 6 5 4 3 2 1 0
0 – Disable SOD 1 – Enable SOD
Serial Output Data

## Slide 239: RIM and Serial Input
Again, the RIM instruction has dual use
– Reading the current settings of the Interrupt
Masks
– Serial Data Input
Serial Input Data
The figure below shows how the RIM instruction uses the Accumulator for Serial Input
SDI | P7.5 | P6.5 | P5.5 | IE | M7.5 | M6.5 | M5.5
7 6 5 4 3 2 1 0

## Slide 240: Ports?
Using the SOD and SID pins, the user would not need to bother with setting up input and output ports.
  The two pins themselves can be considered as the ports.
  The instructions SIM and RIM are similar to the OUT and IN instructions except that they only deal with the 1-bit SOD and SID ports.

## Slide 241: Example
Transmit an ASCII character stored in register B using the SOD line.
SODDATA | MVI XRA | C, 0BH A | ; Set up counter for 11 bits ; Clear the Carry flag
NXTBIT | MVI | A, 80H | ; Set D7 =1
 | RAR |  | ; Bring Carry into D7 and set D6 to 1
 | SIM |  | ; Output D7 (Start bit)
CALL BITTIME
STC ; Set Carry to 1 MOV A, B
RAR
; Place character in A
; Shift D0 of the character to the carry Shift 1 into bit D7
; Save the interim result
; decrement bit counter
MOV B, A
DCR C
JNZ NXTBIT

## Slide 242
1
PORT A
EN
PORT
C
EN
PORT B
EN
CONTROL
EN
INTE RNAL
DEC
ODIN G
RD
WR
RD
REGISTER WR
RD
WR
11
10 C
01 B
00 A
00
10
01
WR
CS
A1 A0
8
2
5
5
A
PORT A
CU
PORT C CL
PORT B

## Slide 243: CONTROL WORD
D7 D6 D5 D4 D3 D2
D1 D0
0/1
BSR MODE
BIT SET/RESET FOR PORT C
NO EFFECT ON I/O
MODE
I/O MODE
MODE 0
1
SIMPLE I/O FOR PORTS
A, B AND C
MODE 1
HANDSHAKE I/O FOR PORTS A AND/OR B
PORT C BITS ARE USED FOR HANDSHAKE
MODE 2
BIDIRECTI ONAL DATA BUS FOR PORT A
PORT B EITHER IN MODE 0 OR
1
PORT C BITS ARE USED FOR HANDSHAK E

## Slide 244: 8255A
GROUP A PORT A
(8)
GROUP B PORT B
(8)
GROUPA
PORT C UPPER (4)
GROUPB PORT C LOWER (4)
GROUP A
CON- TROL
GROUP B
CON- TROL
READ/ WRITE CONTROL LOGIC
DATA BUS BUFFER
BIDIRECTION AL DATA BUS
D1,D0
RD
WR
A1 A0
RESET
8-BIT INTERNAL DATA BUS
I/O
PA7-PA0
I/O
PC7-PC4
I/O
PC3- PC0
I/O
PB7- PB0
+5V
1
CS
GND
POWER SUPPLIES

## Slide 245: Control Word Format for I/O Mode
1
D7 D6 D5 D4 D3 D2 D1 D0
1= I/O Mode
0= BSR Mode
Group B
PORT CL (PC3-PC0) 1= INPUT;0= OUTPUT PORT B
1= INPUT;0= OUTPUT
MODE SELECTION 0=MODE0; 1=MODE 1
Group A
PORT CU (PC7-PC4)
1= INPUT; 0=OUTPUT
PORT A
1= INPUT; 0=OUTPUT MODE SELECTION
00= MODE 0;01= MODE 1;1X= MODE 2

## Slide 246
WR RESET
PA7
PA0 PC7
PC4 8255A PC3
PC0 PB7
PB0
CS A1
A0 RD
1

## Slide 247: Mode 0 ( Simple Input or Output )
PROBLEM 1)
Interface 8255a to a 8085 microprocessor using I/O-mapped - I/O technique so that Port a have address 80H in the system.
Determine addresses of Ports B,C and control register.
Write an ALP to configure port A and port CL as output ports and port B and port CU as input ports in mode 0.
Connect DIP switches connected to the to input ports and LEDs to the output ports .
Read switch positions connected to port A and turn on the respective LEDs of port b. Read switch positions of port CL and display the reading at port CU
1

## Slide 248: BSR (Bit Set/Reset ) Mode
D7 D6
D5
BSR control word
D4 D3
D2
D1
D0
0
X
X
X
BIT SELECT
S/R
BSR Mode
1
Not used, Generally reset to 0
000 = Bit 0
001 = Bit 1
010 = Bit 2
011 = Bit 3
100 = Bit 4
101 = Bit 5
110 = Bit 6
111 = Bit 7
1= Set
0 = Reset

## Slide 249: Problem 2)
Write an ALP to set bits PC7 and PC 3 and reset them after 10 ms in BSR mode.
1

## Slide 250: Mode 1: Input or Output with Handshake
1
PC4
PC5
PC3
PC2
PC1
PC0
Port A Input
Port B Input
STBA
IBFA
INTRA
STBB
IBFB
INTRB
INTEA
INTEB
I/O
PC 6,7
RD
PA7-PA0
PB7-PB0
Port A with
Handshake Signal
Port b with Handshake Signal
Port A & Port B as
Input in Mode 1

## Slide 251: Control word – mode 1 input
1
D7 D6
D5
D4
D3
D2
D1
D0
x
1
1
1
1
0
1
1/0
I/O Mode
Port A
Mode 1
Port A Input
Port B Input Port B Mode 1
PC6,7
1=Input; 0=Output

## Slide 252: Status Word – Mode 1 input
1
D7 D6
D5
D4
D3
D2
D1
D0
INTRB
IBFB
INTEA
IBFA
I/O I/O
INTRA
INTEB

## Slide 253
STB
IBF
INTR
RD
Input from peripheral 1
v

## Slide 254: INTEA
1
PC7
PC6
PC3
PC2
PC1
PC0
OBFA
ACKA
INTRA
OBFB
ACKB
INTEB
PC 4,5
WR
PA7-PA0
Port A with Handshake
Signal
Port b with
Handshake Signal
Port A Output
INTRB
Port B Output PB7-PB0
I/O
Port A & B as Output
In Mode 1

## Slide 255: Control word – mode 1 Output
1
D7 D6
D5
D4
D3
D2
D1
D0
x
0
1
0
1
0
1
1/0
I/O Mode
Port A
Mode 1
Port A
Output
Port B Output Port B Mode 1
PC4,5
1=Input; 0=Output

## Slide 256: Status Word – Mode 1 Output
1
D7 D6
D5
D4
D3
D2
D1
D0
INTRB
OBFB
INTEa I/O
OBFA
I/O INTRA INTEB

## Slide 257
1
WR
OBF
INTR
ACK
output

## Slide 258: Status
Initialize Ports
Read port C for status
Is Peripheral Ready?
Interrupt
Initialize Ports
Enable INTE
No
1
Continue
yes
No
Yes
Continue

## Slide 259: Problem 3)
Initialize 8255A in mode 1 to configure Port A as an input port and Port B as an output port.
Assuming that an A-to-d converter is connected with port A as an interrupt I/O
and a printer is connected with port B as a status check I/O
1

## Slide 260: 8086 MICROPROCESSOR

## Slide 261: Pinouts
I-46

## Slide 262: 8086 Pins
I-47
The 8086 comes in a 40 pin package which means that some pins have more than one use or are multiplexed. The packaging technology of time limited the number of pin that could be used.
In particular, the address lines 0 - 15 are multiplexed with data lines 0-15, address lines 16-19 are multiplexed with status lines. These pins are
AD0 - AD15, A16/S3 - A19/S6
The 8086 has one other pin that is multiplexed and this is BHE’/S7. BHE stands for Byte High Enable. This is an active low signal that is asserted when there is data on the upper half of the data bus.
The 8086 has two modes of operation that changes the function of some pins. The SDK-86 uses the 8086 in the minimum mode with the MN/MX’ pin tied to 5 volts. This is a simple single processor mode. The IBM PC uses an 8088
in the maximum mode with the MN/MX” pin tied to ground. This is the mode required for a coprocessor like the 8087.

## Slide 263: 8086 Pins
I-48
In the minimum mode the following pins are available.
HOLD
When this pin is high, another master is requesting control of the local bus, e.g., a DMA controller.
HLDA
HOLD Acknowledge: the 8086 signals that it is going to float the local bus.
WR’
Write: the processor is performing a write memory or I/O operation.
M/IO’
Memory or I/O operation.
DT/R’
Data Transmit or Receive.
DEN’
Data Enable: data is on the multiplexed address/data pins.
ALE Address Latch Enable: the address is on the address/data pins.
This signal is used to capture the address in latches to establish the address bus.
INTA’
Interrupt acknowledge: acknowledges external interrupt requests.

## Slide 264: 8086 Pins
I-49
The following are pins are available in both minimum and maximum modes.
VCC + 5 volt power supply pin.
GND Ground
RD’ READ: the processor is performing a read memory or I/O operation.
READY Acknowledgement from wait-state logic that the data transfer will be completed.
RESET
Stops processor and restarts execution from FFFF:0. Must be high for 4 clocks. CS = 0FFFFH, IP = DS = SS = ES = Flags = 0000H, no other registers are affected.
TEST’
The WAIT instruction waits for this pin to go low. Used with 8087.
NMI
Non Maskable Interrupt: transition from low to high causes an interrupt. Used for emergencies such as power failure.
INTR
Interrupt request: masked by the IF bit in FLAG register.
CLK Clock: 33% duty cycle, i.e., high 1/3 the time.

## Slide 265: 8086 Features
I-8
16-bit Arithmetic Logic Unit
16-bit data bus (8088 has 8-bit data bus)
20-bit address bus - 220 = 1,048,576 = 1 meg
The address refers to a byte in memory. In the 8088, these bytes come in on the 8-bit data bus. In the 8086, bytes at even addresses come in on the low half of the data bus (bits 0-7) and bytes at odd addresses come in on the upper half of the data bus (bits 8-15).
The 8086 can read a 16-bit word at an even address in one operation and at an odd address in two operations. The 8088 needs two operations in either case.
The least significant byte of a word on an 8086 family microprocessor is at the lower address.

## Slide 266: 8086 Architecture
I-9
The 8086 has two parts, the Bus Interface Unit (BIU) and the Execution Unit (EU).
The BIU fetches instructions, reads and writes data, and computes the 20-bit address.
The EU decodes and executes the instructions using the 16-bit ALU.
The BIU contains the following registers: IP - the Instruction Pointer
CS - the Code Segment Register DS - the Data Segment Register SS - the Stack Segment Register ES - the Extra Segment Register
The BIU fetches instructions using the CS and IP, written CS:IP, to contruct the 20-bit address. Data is fetched using a segment register (usually the DS) and an effective address (EA) computed by the EU depending on the addressing mode.

## Slide 267: 8086 Block Diagram
I-10

## Slide 268: 8086 Architecture
The EU contains the following 16-bit registers:
AX - the Accumulator BX - the Base Register CX - the Count Register DX - the Data Register
SP - the Stack Pointer
\ defaults to stack segment
BP - the Base Pointer /
SI - the Source Index Register DI - the Destination Register
These are referred to as general-purpose registers, although, as seen by their names, they often have a special-purpose use for some instructions.
The AX, BX, CX, and DX registers can be considers as two 8-bit registers, a High byte and a Low byte. This allows byte operations and compatibility with the previous generation of 8-bit processors, the 8080 and 8085. 8085 source code could be translated in 8086 code and assembled. The 8-bit registers are:
AX --> AH,AL BX --> BH,BL CX --> CH,CL DX --> DH,DL
I-11

## Slide 269: Flag Register
 | NT | IOPL | OF | DF | IF | TF | SF | ZF |  | AF |  | PF |  | CF
Flag register contains information reflecting the current status of a microprocessor. It also contains information which controls the operation of the microprocessor.
15 0
Control Flags
Status Flags
IF:
DF:
TF:
Interrupt enable flag Direction flag
Trap flag
CF:
PF:
AF:
ZF:
SF:
OF:
NT: IOPL:
Carry flag Parity flag
Auxiliary carry flag Zero flag
Sign flag Overflow flag Nested task flag
Input/output privilege level

## Slide 270: Flags Commonly Tested During the Execution of Instructions
There are five flag bits that are commonly tested during the execution of instructions
  Sign Flag (Bit 7), SF: 0 for positive number and 1 for negative number
Zero Flag (Bit 6), ZF:
If the ALU output is 0, this bit is set (1); otherwise, it is 0
Carry Flag (Bit 0), CF: It contains the carry generated during the execution
Auxiliary Carry, AF:
(Bit 4)
Depending on the width of ALU inputs, this flag bit contains the carry generated at bit 3 (or, 7, 15) of the 8088 ALU
Parity Flag (bit2), PF:
It is set (1) if the output of the ALU has even number of ones; otherwise it is zero

## Slide 271: Direction Flag
Direction Flag (DF) is used to control the way SI and DI are adjusted during the execution of a string instruction
  DF=0, SI and DI will auto-increment during the execution; otherwise, SI and DI auto-decrement
  Instruction to set DF: STD; Instruction to clear DF: CLD
  Example:
CLD
MOV CX, 5 REP MOVSB
At the beginning of execution, DS=0510H and SI=0000H
53
48
4F
50
50
45
52
S H
O
P P
E R
DS : SI 0510:0000
0510:0001
0510:0002
0510:0003
0510:0004
0510:0005
0510:0006
Source String
SI CX=5
SI CX=4
SI CX=3
SI CX=2
SI CX=1
SI
CX=0

## Slide 272: 8086 Programmer’s Model
ES
CS
SS
DS
IP
AH | AL
BH | BL
CH | CL
DH | DL
SP | 
BP | 
SI | 
DI | 
FLAGS | 
AX BX
CX DX
Extra Segment Code Segment
Stack Segment Data Segment Instruction Pointer
Accumulator Base Register
Count Register Data Register Stack Pointer Base Pointer
Source Index Register Destination Index Register
I-13
BIU registers (20 bit adder)
EU registers
16 bit arithmetic

## Slide 273: Memory Address Calculation
Segment addresses must be stored in segment registers
Offset is derived from the combination of pointer registers, the Instruction Pointer (IP), and immediate values
0000
+
Segment address
Offset
Memory address
Examples
3 | 4 | 8 | A | 0
 | 4 | 2 | 1 | 4
3 | 8 | A | B | 4
CS IP +
Instruction address
5 | 0 | 0 | 0 | 0
 | F | F | E | 0
5 | F | F | E | 0
SS SP +
Stack address
1 | 2 | 3 | 4 | 0
 | 0 | 0 | 2 | 2
1 | 2 | 3 | 6 | 2
DS DI +
Data address

## Slide 274: Segments
EEE/CSE 226
Segment Registers
CODE
STACK
DATA
EXTRA
MEMORY
Address 0H
0FFFFFH
64K Data Segment
64K Code Segment
Segments are < or = 64K,
can overlap, start at an address that ends in 0H.
I-14
 CS:0
Segment Starting address is segment register value shifted 4 places to the left.

## Slide 275: 8086 Memory Terminology
DATA
STACK
EXTRA
CODE
0100H
0B200H
0CF00H
0FF00H
DS:
SS:
ES:
CS:
01000H
10FFFH
I-15
0B2000H
0C1FFFH
0CF000H
0DEFFFH
0FF000H
0FFFFFH
0H
Segment Registers
Memory Segments
Segments are < or = 64K and can overlap.
Note that the Code segment is < 64K since 0FFFFFH is the highest address.

## Slide 276: The Code Segment
Memory
Segment Register
Offset
Physical or Absolute Address
0
+
I-16
CS:
IP
0400H
0056H
4000H
4056H
0400
0056
04056H
The offset is the distance in bytes from the start of the segment. The offset is given by the IP for the Code Segment.
Instructions are always fetched with using the CS register.
The physical address is also called the absolute address.
CS:IP = 400:56
Logical Address
0H
0FFFFFH

## Slide 277: The Stack Segment
Memory
Segment Register
Offset
Physical Address
+
I-17
SS:
SP
0A00
0100
0A000H
0A100H
0A00
0
0100
0A100H
The offset is given by the SP register.
The stack is always referenced with respect to the stack segment register. The stack grows toward decreasing memory locations.
The SP points to the last or top item on the stack.
PUSH - pre-decrement the SP POP - post-increment the SP
SS:SP
0H
0FFFFFH

## Slide 278: The Data Segment
Memory
Segment Register
Offset
Physical Address
+
I-18
DS:
EA
05C0
0050
05C00H
05C50H
05C0
0
0050
05C50H
Data is usually fetched with respect to the DS register. The effective address (EA) is the offset.
The EA depends on the addressing mode.
DS:EA
0H
0FFFFFH

## Slide 279: 8086 memory Organization

## Slide 280
Even addresses are on the low half of the data bus (D0-D7).
Odd addresses are on the upper half of the data bus (D8-D15).
A0 = 0 when data is on the low half of the data bus.
BHE’ = 0 when data is on the upper half of the data bus.

## Slide 281: MAX and MIN Modes
In minmode, the 9 signals correspond to control signals that are needed to operate memory and I/O devices connected to the 8088.
In maxmode, the 9 signals change their functions; the 8088 now requires the use of the 8288 bus controller to generate memory and I/O read/write signals.

## Slide 282: Why MIN and MAX modes?
Minmode signals can be directly decoded by memory and I/O circuits, resulting in a system with minimal hardware requirements.
Maxmode systems are more complicated, but obtain the new signals that allow for bus grants (e.g. DMA), and the use of an 8087 coprocessor.

## Slide 283: The 9 pins (min)
**ALE: address latch enable (AD0 – AD7)
**DEN: data enable (connect/disc. buffer)
**WR: write (writing indication)
*HOLD
*HDLA: hold acknowledge
*INTA: interrupt acknowledge
IO/M: memory access or I/O access
DT/R: data transmit / receive (direction)
SSO: status

## Slide 284: The 9 pins (max)
S0, S1, S2: status
*RQ/GT0, RQ/GT1: request/grant
*LOCK: locking the control of the sys. bus
*QS1, QS0: queue status (tracking of internal instruction queue).
HIGH

## Slide 285: Instruction Types
Data transfer instructions
String instructions
Arithmetic instructions
Bit manipulation instructions
Loop and jump instructions
Subroutine and interrupt instructions
Processor control instructions

## Slide 286: Addressing Modes
Immediate addressing
Register addressing
Direct addressing
Register Indirect addressing
Based addressing
Indexed addressing
Based indexed addressing
Based indexed with displacement addressing
MOV AL, 12H MOV AL, BL MOV [500H], AL MOV DL, [SI] MOV AX, [BX+4] MOV [DI-8], BL MOV [BP+SI], AH
MOV CL, [BX+DI+2]
Exceptions
String addressing
Port addressing (e.g. IN AL, 79H)
Addressing Modes
Examples

## Slide 287: Data Transfer Instructions
MOV Destination, Source
  Move data from source to destination; e.g. MOV [DI+100H], AH
  It does not modify flags
For 80x86 family, directly moving data from one memory location to another memory location is not allowed
MOV [SI], [5000H]
When the size of data is not clear, assembler directives are used
MOV [SI], 0
BYTE PTR
WORD PTR
DWORD PTR
MOV BYTE PTR [SI], 12H MOV WORD PTR [SI], 12H MOV DWORD PTR [SI], 12H
You can not move an immediate data to segment register by MOV MOV DS, 1234H

## Slide 288: Instructions for Stack Operations
What is a Stack ?
  A stack is a collection of memory locations. It always follows the rule of last-in-firs-out
  Generally, SS and SP are used to trace where is the latest date written into stack
PUSH Source
  Push data (word) onto stack
  It does not modify flags
— For Example: PUSH AX
(assume ax=1234H, SS=1000H, SP=2000H
before PUSH AX)
??
??
??
??
1000:1FFD
1000:1FFE
1000:1FFF
1000:2000
1000:1FFE
1000:1FFF
1000:2000
1000:1FFD
??
34
12
??
SS:SP
SS:SP
Before PUSH AX, SP = 2000H After PUSH AX, SP = 1FFEH
AX
12
34
Decrementing the stack pointer during a push is a standard way of implementing stacks in hardware

## Slide 289: Instructions for Stack Operations
PUSHF
  Push the values of the flag register onto stack
  It does not modify flags
POP Destination
  Pop word off stack
  It does not modify flags
  For example: POP AX
??
34
12
EC
1000:1FFD
1000:1FFE
1000:1FFF
1000:2000
1000:1FFE
1000:1FFF
1000:2000
1000:1FFD
??
34
12
EC
SP
SP
Before POP, SP = 1FFEH
After POP AX,
SP = 2000H
AX
12
34
POPF
  Pop word from the stack to the flag register
  It modifies all flags

## Slide 290: Data Transfer Instructions
SAHF
  Store data in AH to the low 8 bits of the flag register
  It modifies flags: AF, CF, PF, SF, ZF
LAHF
  Copies bits 0-7 of the flags register into AH
  It does not modify flags
LDS Destination Source
  Load 4-byte data (pointer) in memory to two 16-bit registers
  Source operand gives the memory location
  The first two bytes are copied to the register specified in the destination operand; the second two bytes are copied to register DS
  It does not modify flags
LES Destination Source
  It is identical to LDS except that the second two bytes are copied to ES
  It does not modify flags

## Slide 291: Data Transfer Instructions
LEA Destination Source
  Transfers the offset address of source (must be a memory location) to the destination register
  It does not modify flags
XCHG Destination Source
  It exchanges the content of destination and source
  One operand must be a microprocessor register, the other one can be a register or a memory location
  It does not modify flags
XLAT
  Replace the data in AL with a data in a user defined look-up table
  BX stores the beginning address of the table
  At the beginning of the execution, the number in AL is used as the index of the look-up table
  It does not modify flags

## Slide 292: String Instructions
String is a collection of bytes, words, or long-words that can be up to 64KB in length
String instructions can have at most two operands. One is referred to as source string and the other one is called destination string
  Source string must locate in Data Segment and SI register points to the current element of the source string
  Destination string must locate in Extra Segment and DI register points to the current element of the destination string
53
48
4F
50
50
45
52
S H
O
P P
E R
DS : SI 0510:0000
0510:0001
0510:0002
0510:0003
0510:0004
0510:0005
0510:0006
53
48
4F
50
50
49
4E
S H
O
P P
I N
ES : DI 02A8:2000
02A8:2001
02A8:2002
02A8:2003
02A8:2004
02A8:2005
02A8:2006
Source String
Destination String

## Slide 293: Repeat Prefix Instructions
REP String Instruction
  The prefix instruction makes the microprocessor repeatedly execute the string instruction until CX decrements to 0 (During the execution, CX is decreased by one when the string instruction is executed one time).
  For Example:
MOV CX, 5 REP MOVSB
By the above two instructions, the microprocessor will execute MOVSB 5 times.
  Execution flow of REP MOVSB::
While (CX!=0)
{
CX = CX –1; MOVSB;
}
Check_CX: If CX!=0 Then
CX = CX –1; MOVSB;
goto Check_CX; end if
OR

## Slide 294: String Instructions
MOVSB (MOVSW)
  Move byte (word) at memory location DS:SI to memory location ES:DI and update SI and DI according to DF and the width of the data being transferred
  It does not modify flags
—Example:
Source String
Destination String
MOV AX, 0300H
 | DS : SI |  |  | ES : DI
MOV AX, 0510H | 0510:0000 | 53 | S | 0300:0100
MOV DS, AX | 0510:0001 | 48 | H | 
MOV SI, 0 | 0510:0002 | 4F | O | 
MOV ES, AX | 0510:0003 | 50 | P | 
MOV DI, 100H | 0510:0004 | 50 | P | 
CLD | 0510:0005 | 45 | E | 
MOV CX, 5 | 0510:0006 | 52 | R | 
REP MOVSB

## Slide 295: String Instructions
CMPSB (CMPSW)
  Compare bytes (words) at memory locations DS:SI and ES:DI;
update SI and DI according to DF and the width of the data being compared
  It modifies flags
—Example:
Assume:
ES = 02A8H DI = 2000H DS = 0510H SI = 0000H
CLD
MOV CX, 9 REPZ CMPSB
What’s the values of CX after The execution?
53
48
4F
50
50
45
52
S H
O
P P
E R
DS : SI 0510:0000
0510:0001
0510:0002
0510:0003
0510:0004
0510:0005
0510:0006
ES : DI 02A8:2000
02A8:2001
02A8:2002
02A8:2003
02A8:2004
02A8:2005
02A8:2006
Source String
Destination String
53
48
4F
50
50
49
4E
S H
O
P P
I N

## Slide 296: String Instructions
SCASB (SCASW)
  Move byte (word) in AL (AX) and at memory location ES:DI; update DI according to DF and the width of the data being compared
  It modifies flags
LODSB (LODSW)
  Load byte (word) at memory location DS:SI to AL (AX);
update SI according to DF and the width of the data being transferred
  It does not modify flags
STOSB (STOSW)
  Store byte (word) at in AL (AX) to memory location ES:DI;
update DI according to DF and the width of the data being transferred
  It does not modify flags

## Slide 297: Repeat Prefix Instructions
REPZ String Instruction
  Repeat the execution of the string instruction until CX=0 or zero flag is clear
REPNZ String Instruction
  Repeat the execution of the string instruction until CX=0 or zero flag is set
REPE String Instruction
  Repeat the execution of the string instruction until CX=0 or zero flag is clear
REPNE String Instruction
  Repeat the execution of the string instruction until CX=0 or zero flag is set

## Slide 298: Loops and Conditional Jumps
I-39
All loops and conditional jumps are SHORT jumps, i.e., the target must be in the range of an 8-bit signed displacement (-128 to +127).
The displacement is the number that, when added to the IP, changes the IP to point at the jump target. Remember the IP is pointing at the next instruction when this occurs.
The loop instructions perform several operations at one time but do not change any flags.
LOOP decrements CX and jumps if CX is not zero.
LOOPNZ or LOOPNE -- loop while not zero or not equal: decrements CX and jumps if CX is not zero or the zero flag ZF = 0.
LOOPZ or LOOPE -- loop while zero or equal: decrements CX and jumps if CX is zero or the zero flag ZF = 1.
The conditional jump instructions often follow a compare CMP or TEST instruction. These two instructions only affect the FLAG register and not the destination. CMP does a SUBtract (dest - src) and TEST does an AND.
For example, if a CMP is followed by a JG (jump greater than), then the jump is taken if the destination is greater than the source.
Test is used to see if a bit or bits are set in a word or byte such as when determining the status of a peripheral device.

## Slide 299: Conditional Jumps
I-40
Name/Alt | Meaning | Flag setting
JE/JZ | Jump equal/zero | ZF = 1
JNE/JNZ | Jump not equal/zero | ZF = 0
JL/JNGE | Jump less than/not greater than or = | (SF xor OF) = 1
JNL/JGE | Jump not less than/greater than or = | (SF xor OF) = 0
JG/JNLE | Jump greater than/not less than or = | ((SF xor OF) or ZF) = 0
JNG/JLE | Jump not greater than/ less than or = | ((SF xor OF) or ZF) = 1
JB/JNAE | Jump below/not above or equal | CF = 1
JNB/JAE | Jump not below/above or equal | CF = 0
JA/JNBE | Jump above/not below or equal | (CF or ZF) = 0
JNA/JBE | Jump not above/ below or equal | (CF or ZF) = 1
JS | Jump on sign (jump negative) | SF = 1
JNS | Jump on not sign (jump positive) | SF = 0
JO | Jump on overflow | OF = 1
JNO | Jump on no overflow | OF = 0
JP/JPE | Jump parity/parity even | PF = 1
JNP/JPO | Jump no parity/parity odd | PF = 0
JCXZ | Jump on CX = 0 | ---

## Slide 300: 8254 Internal Architecture
8
Counter
=0
Counter
=1
Counter
=2
Control Word Register
Read/ Write Logic
Data Bus Buffer
CLK 0
GATE 0
OUT 0
CLK 1
GATE 1
OUT 1
CLK 2
GATE 2
OUT 2
RD
WR
A0 A1
CS
D7-D0

## Slide 301: THE CONTROL WORD REGISTER AND COUNTERS ARE SELECTED ACCORDING TO THE SIGNALS ON LINE A0 and A1 AS SHOWN BELOW
A1 A0 Selection
0 0 Counter 0
1 Counter 1
0 Counter 2
1 1 Control Register

## Slide 302: 8254 Control Word Format
 | SC1 |  |  | SC0 |  |  | RW1 |  |  | RW0 |  |  | M2 |  |  | M1 |  |  | M0 |  |  | BCD | 
SC1 SC0
0
0
Select counter 0
0
1
Select counter 1
1
0
Select Counter 2
1
1
Read-Back command
RW1
RW0
0
0
Counter Latch Command
0
1
Read/Write least significant byte only
1
0
Read/Write most significant byte only
1
1
Read/Write least significant byte first, Then the most significant byte.

## Slide 303: BCD:
0 | Binary Counter 16-bits
1 | Binary Coded Decimal (BCD) Counter

## Slide 304
 | M2 |  |  | M1 |  |  | M0 |  |  |  | 
 | 0 |  |  | 0 |  |  | 0 |  |  | Mode 0 | 
 | 0 |  |  | 0 |  |  | 1 |  |  | Mode 1 | 
 | X |  |  | 1 |  |  | 0 |  |  | Mode 2 | 
 | X |  |  | 1 |  |  | 1 |  |  | Mode 3 | 
 | 1 |  |  | 0 |  |  | 0 |  |  | Mode 4 | 
 | 1 |  |  | 0 |  |  | 1 |  |  | Mode 5 | 

## Slide 305: MODE 0 : Interrupt on terminal count
Clk
3
2
1
0
WR
Output Interrupt

## Slide 306: MODE 1 : HARDWARE-RETRIGGERABLE ONE-SHOT
Clk
WR
3
2
1
0
Output

## Slide 307: MODE 2 : RATE GENERATOR CLOCK
 |  | 3 | 2 | 1 | 0
Clk
WR
3
OUTPUT

## Slide 308: MODE 3 : Square Wave Generator
Clk
4
2
4
2
4
2
4
2
OUTPUT(n=4)
 | 5 | 4 | 2 | 5 | 2 | 5 | 4 | 2
OUTPUT(n=5)

## Slide 309
MODE 4 : SOFTWARE TRIGGERED STROBE
In this mode OUT is initially high; it goes low for one clock period at the end of the count. The count must be RELOADED -(UNLIKE MODE 2)
for subsequent outputs.

## Slide 310: MODE 5 : HARWARE TRIGGERED STROBE
This mode is similar to MODE 4 except that it is triggered by the rising pulse at the gate. Initially, the OUT is low and when the GATE pulse is triggered from low to high , the count begins. At the end of the count the OUT goes low for one clock period.

## Slide 311: READ BACK COMMAND FORMAT:
THIS FEATURE AVAILABLE ONLY IN 8254 and not in 8253.
1
1
COU STAT CNT2 CNT1 CNT0 NT US
0

## Slide 312: Data Transfer Schemes

## Slide 313: Why do we need data transfer schemes ?
Availability of wide variety of I/O devices because of variations in manufacturing technologies e.g. electromechanical, electrical, mechanical, electronic etc.
Enormous variation in the range of speed.
Wide variation in the format of data.
•

## Slide 314: Classification of Data Transfer Schemes
Data transfer schemes
Programmed Data transfer
DMA
Data transfer
Synchronous mode
Asynchronous mode
Interrupt Driven mode
Block DMA mode
Cycle stealing DMA mode

## Slide 315: Programmed Data Transfer Scheme
The data transfer takes place under the control of a program residing in the main memory.
These programs are executed by the CPU when an I/O device is ready to transfer data.
To transfer one byte of data, it needs to execute several instructions.
This scheme is very slow and thus suitable when small amount of data is to be transferred.

## Slide 316: Synchronous Mode of Data Transfer
Its used for I/O devices whose timing characteristics are fast enough to be compatible in speed with the communicating MPU.
In this case the status of the I/O device is not checked before data transfer.
The data transfer is executed using IN and OUT instructions.

## Slide 317
Memory compatible with MPU are available. Hence this method is invariably used with compatible memory devices.
The I/O devices compatible in speed with MPU are usually not available. Hence this technique is rarely used in practice

## Slide 318: Asynchronous Data Transfer
This method of data transfer is also called Handshaking mode.
This scheme is used when speed of I/O device does not match with that of MPU and the timing characteristics are not predictable.
The MPU fist sends a request to the device and then keeps on checking its status.

## Slide 319
The data transfer instructions are executed only when the I/O device is ready to accept or supply data.
Each data transfer is preceded by a requesting signal sent by MPU and READY signal from the device.

## Slide 320: Disadvantages
A lot of MPU time is wasted during looping to check the device status which may be prohibitive in many situations.
Some simple devices may not have status signals. In such a case MPU goes on checking whether data is available on the port or not.

## Slide 321: Interrupt Driven Data Transfer
In this scheme the MPU initiates an I/O device to get ready and then it executes its main program instead of remaining in the loop to check the status of the device.
When the device gets ready, it sends a signal to the MPU through a special input line called an interrupt line.
The MPU answers the interrupt signal after executing the current instruction.

## Slide 322
The MPU saves the contents of the PC on the stack first and then takes up a subroutine called ISS (Interrupt Service Subroutine).
After returning from ISS the MPU again loads the PC with the address that is just loaded in the stack and thus returns to the main program.
It is efficient because precious time of MPU is not wasted while the I/O device gets ready.
In this scheme the data transfer may also be initiated by the I/O device.

## Slide 323: Multiple Interrupts
The MPU has one interrupt level and several I/O devices to be connected to it which are attended in the order of priority.
The MPU has several interrupt levels and one I/O device is to be connected to each interrupt level.

## Slide 324
The MPU has several interrupt levels and more than one I/O devices are to be connected to each interrupt level.
The MPU executes multiple interrupts by using a device polling technique to know which device connected to which interrupt level has interrupted

## Slide 325: Interrupts of 8085
On the basis of priority the interrupt signals are as follows
TRAP
RST 7.5
RST6.5
RST5.5
INTR
These interrupts are implemented by the hardware

## Slide 326: Interrupt Instructions
EI ( Enable Interrupt) This instruction sets the interrupt enable Flip Flop to activate the interrupts.
DI ( Disable Interrupt) This instruction resets the interrupt enable Flip Flop and deactivates all the interrupts except the non-maskable interrupt i.e. TRAP
RESET This also resets the interrupt enable Flip Flop.

## Slide 327
SIM (Set Interrupt Mask) This enables\disables interrupts according to the bit pattern in accumulator obtained through masking.
RIM (Read Interrupt Mask) This instruction helps the programmer to know the current status of pending interrupt.

## Slide 328: Call Locations and Hex – codes
for RST n
RST n | Hex - code | Call location
RST 0 | C7 | 0000
RST 1 | CF | 0008
RST 2 | D7 | 0010
RST 3 | DF | 0018
RST 4 | E7 | 0020
RST 5 | EF | 0028
RST 6 | F7 | 0030
RST 7 | FF | 0038
These instructions are implemented by the software

## Slide 329: DMA Data Transfer scheme
Data transfer from I/O device to memory or vice-versa is controlled by a DMA controller.
This scheme is employed when large amount of data is to be transferred.
The DMA requests the control of buses through the HOLD signal and the MPU acknowledges the request through HLDA signal and releases the control of buses to DMA.
It’s a faster scheme and hence used for high speed printers.

## Slide 330: Block mode of data transfer
In this scheme the I/O device withdraws the DMA request only after all the data bytes have been transferred.
Cycle stealing technique
In this scheme the bytes are divided into several parts and after transferring every part the control of buses is given back to MPU and later stolen back when MPU does not need it.